## Slide 1
SHORING

## Slide 2
General
Load Spreading
Shoring Categories
Student Activity
OVERVIEW

## Slide 3
GENERAL PURPOSE

## Slide 4
Provides protection
Performance
Contact your affiliated local AMLO/ADACG/UMO about specific shoring requirements
L
Notes:   Provides protection
Protects the aircraft cargo floor and 463L pallet surfaces
Protects aircraft parking ramps
Performance
Increases cargo contact areas for better load distribution
It decreases the approach angle of the aircraft cargo ramps

## Slide 5
LOAD SPREADING

## Slide 6
Load spreading is a physical process that distributes a concentrated weight over a larger area
Weight exerts a certain amount of pressure determined by its supporting contact area

## Slide 7
The contact area is increased at a 45 degree angle from the upper surface of the shoring to the cargo floor

## Slide 8
The increased contact area decreases the pressure on the floor
Important notes:
    Shoring will only increase the area of contact
    Shoring does not increase PSI limitations
S

## Slide 10
Shoring Categories

## Slide 11
  Protects floors and ramps
  Generally not required for most vehicles
ROLLING SHORING
Notes: 1. Use rolling shoring to protect the aircraft parking ramp, and the cargo floor when transporting a vehicle across it
2. Most vehicles shipped by air do not exceed weight limitations, and consequently, do not require rolling shoring

## Slide 12
Protects the floor from vehicles with cleats, studs, or other gripping devices
Note: The minimum thickness of shoring is 1/2 inch f/C17 & C5.
¾ f/C130
Notes: 3. Vehicles with cleats, studs, or other gripping devices and treads that allow concentrated contact require rolling shoring
a) Cleated or lugged wheels can easily cause damage to the aircraft floor or soft surfaces
b) The total weight of the vehicle is transferred to the small, concentrated, contact area of the cleats or lugs
c) Vehicles that have concentrated contacts require rolling shoring thick enough to prevent damage to the cargo floor
d) In all cases, the minimum thickness is ¾ inch

## Slide 14
If you need
rolling shoring,
you will need
parking shoring
PARKING SHORING
Notes: 3. Each aircraft has specific floor weight limitations that apply to wheeled and non-wheeled items of cargo
4. If the vehicle exceeds these weight limitations, you must provide parking shoring before the item can be transported by air
a) General considerations regarding parking shoring you may want to remember when planning an airlift
i. Minimum thickness of parking shoring is ¾ inch
ii. Use parking shoring to protect the aircraft floor or ramps from contact such as blades, buckets, fork-lift tines, steel wheels, trailer tongue supports, etc

## Slide 15
All trailers with a tongue that could rest on the aircraft floor will have parking shoring
Notes: iii. All trailers with a tongue that could rest on the aircraft floor must be shipped with parking shoring, whether connected to or disconnected from its prime mover

## Slide 16
Pneumatic tires do not normally require parking shoring
Notes: iv. Most pneumatic tires do not normally require parking shoring, the tires that do are usually narrow and/or very heavy

## Slide 17
Always use whenever
  there are sharp edges
  or protrusions that could
  damage the aluminum
  surface of a 463L pallets
Contact your local AMLO/ADACG/UMO
  if you are unsure about shoring
  requirements

## Slide 18
Use under frames or axles of vehicles that weigh over 20,000 lbs. and have soft, low pressure, balloon-type, off road tires
SLEEPER SHORING
Notes: 1. Sleeper shoring is used to prevent vertical movement of a vehicle where the tires or suspension system cannot withstand G-loads without failure or depression producing slack in the tiedown devices
2. This prevents the vehicle from bouncing and possibly pulling the tie down rings out of the aircraft floor

## Slide 19
PSI limitations vary according to aircraft
Notes: 3. The base of the sleeper shoring must be large enough to support the entire weight of the vehicle it’s beneath without exceeding the P.S.I. limitation of the aircraft floor
4. P.S.I limitations are variable depending on the type aircraft and location within the aircraft

## Slide 20
  Use approach shoring to decrease the approach angle of aircraft loading ramps
  Some items of cargo may strike the aircraft or ground during loading/offloading operations
APPROACH SHORING

## Slide 22
There is no standard method to calculate how much Approach Shoring is required
These are pieces of equipment that normally require Approach Shoring:
    Most helicopters
    All 40K loaders
    Long vehicles
Notes: 3. Extremely tall and long items may also contact the top of the aircraft cargo compartment without a reduced approach angle provided by approach shoring

## Slide 23
Student Activity
Notes: 3. Extremely tall and long items may also contact the top of the aircraft cargo compartment without a reduced approach angle provided by approach shoring

## Slide 24
ATTLA #1
Notes: 3. Extremely tall and long items may also contact the top of the aircraft cargo compartment without a reduced approach angle provided by approach shoring

## Slide 25
ATTLA #2
Notes: 3. Extremely tall and long items may also contact the top of the aircraft cargo compartment without a reduced approach angle provided by approach shoring

## Slide 27
ATTLA #2 Cont.
Notes: 3. Extremely tall and long items may also contact the top of the aircraft cargo compartment without a reduced approach angle provided by approach shoring

## Slide 29
ATTLA #3
Notes: 3. Extremely tall and long items may also contact the top of the aircraft cargo compartment without a reduced approach angle provided by approach shoring

## Slide 32
QUESTIONS?

## Slide 33
General
Load Spreading
Shoring Categories
Student Activity
SUMMARY