## Slide 1
AIRCRAFT LOAD PLANNING
WEIGHT & BALANCE
CAO: 18 October 19

## Slide 2
Terminology
Weight and Balance Theories
Load Planning
Overview

## Slide 3
TERMINOLOGY

## Slide 4
Reference Datum Line (RDL)
  Imaginary vertical plane at or near the nose of the aircraft

## Slide 5
Fuselage Station (FS)
  Imaginary plane, perpendicular to the longitudinal axis of the aircraft
  Measured in inches from the RDL

## Slide 6
Center of Gravity (CG)
  The point at which an aircraft balances.
  This point is measured in inches from the RDL.
  CG and % of MAC are interchangeable terms

## Slide 7
Gross Weight (GW)
  The total weight of all cargo, passengers, and baggage
  Displayed as “Total Load Weight” in bottom left corner of the Airload Viewer

## Slide 8
Allowable Cabin Load (ACL)
  The maximum planning weight of cargo that may be transported on a specific mission
Standard planning ACLs
  C-130 25,000 lbs.
  C-130J 40,000 lbs.
  C-17 130,000 lbs.
  C-5 M 150,000 lbs.
Notes: Air Force Pamphlet 10-1403 provides standard planning ACLs

## Slide 9
Bulk
Items that fit within the usable dimensions of a single 463L pallet
Notes: 463L Dimensions 108” x 88” x 2.25”
Usable Dimensions 104” x 84”

## Slide 10
Oversize
Items larger than the usable dimensions of a single 463L pallet

## Slide 11
Outsize
Items larger than oversize and can ONLY be airlifted on C-5 or C-17 aircraft

## Slide 12
WEIGHT
AND
BALANCE THEORIES

## Slide 13
Pyramid Method
  Heavy cargo centered with lighter cargo placed out (Recommended method)
C/B
Light
Cargo
Light
Cargo
Heavy Cargo
5000
lbs
1000
lbs
2500
lbs
500
lbs
1000
lbs
2500
lbs
500
lbs
Cargo Load

## Slide 14
50/50 Method
50% of the cargo is placed on either side of the optimum load CG
C/B
1000 lbs.
1000 lbs.
Cargo Load

## Slide 15
EFFECTS of ADDING CARGO
  When cargo is added, the Aircraft CG moves toward the added weight.

## Slide 16
EFFECTS of ADDING CARGO
  When cargo is added, the Aircraft CG moves toward the added weight.

## Slide 17
LOAD SHIFT
  The aircraft’s CG moves with the cargo
  Moving heavy items has a significant change
  Moving light items has a minimal change

## Slide 18
LOAD PLANNING

## Slide 19
Load planning is the process of determining the number and type of aircraft required to transport your units cargo

## Slide 20
Key responsibilities for load planners
DTR Part III, Appendix V
  Aircraft will be loaded to maximum capacity using the ACL, aircraft load specifications, and passenger limits
  Compute weight and balance to ensure fuel efficiency and safety of flight
  Be familiar with proper pallet build up and aircraft contour restrictions
  Be familiar with hazardous material compatibility
    Covered in HAZMAT classes (not air load planners)
Notes: HAZMAT classes go in depth on preparing/certifying hazardous materials.
Load planners must have familiarity with hazardous materials to ensure they are not mixing incompatible cargo on an aircraft.

## Slide 21
Identify Equipment/Personnel for Airlift
Reference ATTLA Certs for applicable equipment
Place equipment on aircraft(s)
Adhere to aircraft limitations
Optimize Aircraft CG
5 STEPS

## Slide 22
Step 1. Identify Equipment / Personnel for airlift
    Option 1 - Equipment Files
      TC-AIMS II (USA & USN)
      SSDM (USMC)
      LOGMOD/GATES (USAF)
    Option 2 – Pull from JECD Library
5 STEPS
Notes: For this class we give you the equipment files, in real world operations you may utilize one or both options.

## Slide 23
Step 2. Reference ATTLA Certs for applicable equipment
Equipment Prep Instructions
Aircraft Loading Instructions
5 STEPS

## Slide 24
Step 3. Start placing equipment on aircraft
  “Pyramid” method or “50/50” method
5 STEPS

## Slide 25
Step 4. Adhere to ALL aircraft limitations
Rolling Stock
  Ease of on-load/off-load (backed in to aircraft)
  Note: unless stated differently in ATTLA cert letter.
  ICODES automatically places vehicle in the right direction
  Trailers loaded on same aircraft and associated/behind Prime Movers
Pallets
  Loaded aft of all rolling stock and passengers
  Aircraft contour restrictions
Baggage
  Pallet require for 20+ personnel (10+ for KC-10)
  Loaded last / first off
Passengers
  Must be 30 inches forward of netted palletized cargo
  Adjacent to cargo restriction (cargo width) for C-130 & C-17
5 STEPS

## Slide 26
Step 5. Optimize Aircraft CG
  Each Airframe has a specific Optimal CG
  Load Shift Principals
    Moving heavy items – Significant Change
    Moving light items – Minimal Change
5 STEPS

## Slide 27
What’s wrong with this picture?
Notes: Prime mover not connected to vehicle.
Passengers within 30” of a pallet.
Improper mix of logistics/aerial delivery pallets.
Vehicle behind pallets.
Vehicle must face forward on the ramp so filler cap is on the high side of ramp.
C/G out of range.

## Slide 28
Advantages
  Offload will be very quick
  Floor loaded cargo space
  Tie-down of vehicles
  CG, optimized
Disadvantages
  Seats lost next to LRS pallets
  LRS pallets can take longer to upload and download
Solution 1:

## Slide 29
Advantages
  Maximized seat availability
  Much easier to marshal vehicles
  Optimized CG
Solution 2:
Disadvantages
  Configuration will take longer
  Lost space for floor loaded cargo

## Slide 30
Do not correct this way:
There is no reason to offset these vehicles:
  You decrease your passenger seat availability.
  Offset cargo has no effect on your C/G.

## Slide 31: QUESTIONS?

## Slide 32
Terminology
Weight and Balance Theories
Load Planning
Summary