## Slide 1
C-130 J & H CHARACTERISTICS

## Slide 2
Cargo Compartment Limitations
Pallet Considerations
Passenger Considerations
C-130H Differences
Load Planning Factors
OVERVIEW
JALP

## Slide 3
Tactical Airlift vs
Strategic Airlift
JALP
Notes: Explain tactical airlift

## Slide 4
COMPARTMENT LIMITATIONS
JALP

## Slide 5
Cargo Floor
  Length – 796” (779” usable)
  Width – 123 (105” usable)
  Height – 108”
Aircraft Ramp
  Length – 127”
  Width – 123” (105” usable)
  Height – 80”
Cargo over 102” requires special loading procedures; contact your AMCU for guidance
JALP
Notes: Cargo over 102” requires special loading procedures; contact your AMCU for guidance

## Slide 6
JALP
Notes: Higher ACLs are possible but only after coordination with your affiliated AMCU or in accordance with the Operation Order

## Slide 7
Aircraft Commander has final authority to accept/reject any or all of the cargo if the planned load is not within bending moment limits
BENDING MOMENTS
(C-130J Only)
JALP
Notes: Use 3.0G if operating in a combat area with hostilities, or tactical maneuvers are planned. Otherwise use 2.5G/2.25G (program defaults to 3.0G)
Bending moment limitation only applies to C- 130J-30

## Slide 8
Within Limits
OUT OF LIMITS
JALP
Notes: Explain bending moment lines and what that white lines are good, red lines are breaking bending moments.

## Slide 9
35” Treadways
35” Treadways
TREADWAY
LIMITATIONS
Treadways begin 15” left and right of aircraft centerline
JALP
Notes: Explain that any axles within 48” must be combined.

## Slide 10
FS 345 - 537
FS 882 - 1017
6,000 lbs Max Axle Weight
TREADWAY
LIMITATIONS
JALP

## Slide 11
FS 537 - 882
13,000 lbs Max Axle Weight
TREADWAY
LIMITATIONS
JALP

## Slide 12
RAMP TREADWAY
LIMITATIONS
Axle only = 3,500 lbs max
FS 1017 – 1141 (Ramp)
Mixed cargo up to 5,000 lbs
(when axle(s) do not exceed
2,500 lbs)
JALP

## Slide 13
FS 345 - 1017
BETWEEN TREADWAY
LIMITATIONS
5,000 lbs Max Axle Weight
2,000 lbs Max Tongue Load
JALP

## Slide 14
FS 1025 – 1141 (Ramp)
1,200 lbs Max Axle Weight
450 lbs Max Tongue Load
BETWEEN TREADWAY
LIMITATIONS
P
JALP

## Slide 15
PALLET CONSIDERATIONS
JALP

## Slide 16
Any cargo above 76” up to 96” high must be placed 12” inboard from the edge of the usable surface of the pallet
Note: Contact your AMCU for cargo above 96”
77”-96”
12” Inset
12” Inset
12” Inset
12” Inset
77”-96”
PALLET POSITIONS 1 & 2
10,355 lbs Max Wt
JALP

## Slide 17
Stowage rack in PP 1 & 2
PALLET POSITIONS 1 & 2
JALP

## Slide 18
96”
Note: Contact AMLO or EAGLE or ADACG for cargo above 96”
96”
10,355 lbs Max Wt
PALLET POSITIONS 3 & 6
JALP
Notes: Maximum weight is 10,355 pounds
Cargo may be loaded over the entire usable surface of the pallet up to 96 inches in height.
No setback needed

## Slide 19
96”
6” Inset
Cargo must be stacked at least 6 inches in from the edge of the usable surface on one 88-inch side.
Note: Contact your AMCU for cargo above 96”
96”
10,355 lbs Max Wt
PALLET POSITIONS 4 & 5
JALP
Notes: Maximum weight is 10,355 pounds
Cargo may be loaded over the entire usable surface of the pallet up to 96 inches in height.
Must have a setback of 6 inches from the edge of the pallet on one 88 inch side for access to wheel well area when combined with the dual rail system (will provide 14 inch aisle way)

## Slide 20
PALLET POSITIONS 4 & 5
JALP

## Slide 21
96”
8,500 lbs Max Wt
PALLET POSITION 7
JALP
Notes: Cargo may be loaded over the entire usable surface of the pallet up to 96 inches in height.

## Slide 22
20” Inset
77”
Cargo must be stacked at least 20 inches in from the edge of the usable surface on one 88-inch side.
5,000 lbs Max Wt
PALLET POSITIONS 8
P
JALP
Notes: Cargo may be stacked up to 77 inches high with a 20 inch set back on the right 88 inch side to give access to rear emergency exits and latrine.
ICODES will not flag pallets over 77 inches (ICODES starts to flag at 81 inches)

## Slide 23
PASSENGER CONSIDERATIONS
JALP

## Slide 24
62
Sidewall Seats
60
Available for use
>40
2 LM’s required
SEATS 1L & 2L AUTOMATICALLY ACCOUNTED FOR
SIDEWALL SEATS
JALP
Notes: 48 permanently installed seats, ONLY 46 available for use
14 optionally installed wheel well seats
One loadmaster will always be seated in the cargo compartment; two with 40 or more passengers
These two seats are accounted for (1L & 2L)

## Slide 25
128
126
Available for use
80
Total seats (66 Optionally installed centerline seats)
Max personnel for prolonged over-water flight
CENTERLINE SEATS
JALP
Notes: 66 Optionally installed centerline seats
128 total seats, 126 available for use
Maximum personnel for prolonged over water flights limited to 80 based on life raft capacity (including crew)

## Slide 26
≤76”
77”- 96”
XXXXXXXXXXXXX
XXXXXXXXXXXXX
XXXXXXXXXXXXX
>96”
OUTSIDE OF WHEEL WELL AREA
PASSENGERS
NEXT TO CARGO
JALP
Notes: Cargo width 76 inches or less; centerline cargo and seat passengers on both sides
Cargo width greater than 76 inches up to 96 inches; offset cargo and seat passengers on opposite side (passengers on one side only)
Cargo width greater than 96 inches- no passengers allowed beside cargo
ICODES will not flag these restrictions

## Slide 27
53”- 72”
X
X
INSIDE OF WHEEL WELL AREA
≤52”
>72”
XXXXXXXXX
PASSENGERS
NEXT TO CARGO
H
JALP
Notes: Cargo width less than 52 inches- centerline cargo and seat passengers on both sides
Cargo width greater than 52 to 72 inches; offset cargo and seat passengers on opposite side (passengers on one side only)
Cargo width greater than 72 inches- no passengers allowed

## Slide 28
C-130H DIFFERENCES
JALP

## Slide 29
Shorter fuselage holds 6 pallets
Restrictions/limitations almost identical to C-130J-30
4 Blades
JALP

## Slide 30
JALP
Notes: Higher ACLs are possible but only after coordination with your affiliated AMCU or in accordance with the Operation Order

## Slide 31
Same restrictions (different FS start/stop)
13,000
3500
6,000
6,000
6,000
6,000
13,000
3500
Max Axle Weight 5,000 Max Tongue load 2,000
Max Axle Weight 1,200
Max Tongue load 450
TREADWAY LIMITATIONS
P
JALP

## Slide 32
76”
10,355 lbs Max Wt
77”- 96”
12” Inset
12” Inset
Any cargo above 76” up to 96” high must be placed 12” inboard from the edge of the usable surface of the pallet
Note: Contact your AMLO or EAGLE or ADACG for cargo above 96”
PALLET POSITION 1
JALP
Notes: Maximum weight is 10,355 pound
Cargo may be loaded over the entire usable surface up to 76”
Any cargo above 76 inches up to 96 inches cargo must be placed 12 inches inboard from the edge of the usable surface of the pallet to accommodate storage racks which can be located on the left, right or both sides of the fuselage.

## Slide 33
PALLET POSITION 1
JALP

## Slide 34
10,355 lbs Max Wt
96”
Note: Contact your AMCU for cargo above 96”
PALLET POSITION 2
JALP
Notes: Maximum weight is 10,355 pounds
Cargo may be loaded over the entire usable surface of the pallet up to 96 inches in height.
No setback needed

## Slide 35
10,355 lbs Max Wt
96”
96”
6” Inset
Cargo must be stacked at least 6 inches in from the edge of the usable surface on one 88-inch side.
PALLET POSITIONS 3 & 4
JALP
Notes: Maximum weight is 10,355 pounds
Cargo may be loaded over the entire usable surface of the pallet up to 96 inches in height.
Must have a setback of 6 inches from the edge of the pallet on one 88 inch side for access to wheel well area when combined with the dual rail system (will provide 14 inch aisl way)

## Slide 36
PALLET POSITIONS 3 & 4
JALP

## Slide 37
8,500 lbs Max Wt
96”
PALLET POSITIONS 5
JALP
Notes: Maximum weight is 8,500 pounds
Cargo may be loaded over the entire usable surface of the pallet up to 96 inches in height.

## Slide 38
4,664 lbs Max Wt
20” Inset
76”
Cargo must be stacked at least 20 inches in from the edge of the usable surface on one 88-inch side.
PALLET POSITIONS 6
P
JALP
Notes: Maximum weight is 4,664 pounds
Cargo may be stacked up to 76 inches high with a 20 inch set back on one 88 inch side to give access to rear emergency exits and latrine.
ICODES will not flag pallets over 76 inches (ICODES does not flag until 81 inches)

## Slide 39
PASSENGER CONSIDERATIONS
JALP

## Slide 40
44
Sidewall Seats
42
Available for use
>40
2 LM’s required
Seats 1L & 15R automatically accounted for
14 OPTIONAL WHEEL WELL SEATS
SIDEWALL SEATS
JALP
Notes: 30 permanently installed seats, ONLY 28 available for use
14 optionally installed wheel well seats
One loadmaster will always be seated in the cargo compartment; two with 40 or more passengers
These two seats are accounted for (1L & 15R)

## Slide 41
92
90
Available for use
80
Total seats (48 Optionally installed centerline seats)
Max personnel for prolonged over-water flight
CENTERLINE SEATS
JALP
Notes: 48 Optionally installed centerline seats
92 total seats, 90 available for use
Maximum personnel for prolonged over water flights limited to 80 based on life raft capacity (including crew)

## Slide 42
Same passenger next to cargo restrictions as C-130J-30
PASSENGERS NEXT TO CARGO
L
JALP
Notes: Cargo width less than 52 inches- centerline cargo and seat passengers on both sides
Cargo width greater than 52 to 72 inches; offset cargo and seat passengers on opposite side (passengers on one side only)
Cargo width greater than 72 inches-no passengers allowed
ICODES will not flag these restrictions

## Slide 43
LOAD PLANNING CONFIGURATIONS
JALP

## Slide 44
Use STD-AL for all variants
AFI 11-2C-130 Vol. 3 Addenda A contains all configuration descriptions
JALP

## Slide 45
Applies to both C-130J-30 and C130H
C-130 J or H
OPTIMAL CG
21% +/- 1%
V
JALP
Notes: Mission planners will manage aviation fuel as a limit commodity and precious resource
Fuel optimization will be considered throughout all phases of mission planning
Load and maintain aircraft at an optimum CG
21% plus or minus 1% of MAC is the optimal CG for C-130H/J

## Slide 46: QUESTIONS?
JALP

## Slide 47
Cargo Compartment Limitations
Pallet Considerations
Passenger Considerations
C-130H Differences
Load Planning Factors
SUMMARY
JALP