## Slide 1: C-17 Characteristics
JALP

## Slide 2
JALP

## Slide 3
Cargo Compartment Limitations
Pallet Considerations
Passenger Considerations
Load Planning Factors
OVERVIEW
JALP

## Slide 4
Capable of tactical (intra-theater) and strategic (inter-theater) airlift
All mission equipment onboard aircraft
Capable of being reconfigured in flight
JALP
C

## Slide 5
CARGO COMPARTMENT LIMITATIONS
JALP

## Slide 6
Cargo Floor
Length: 818”
Cargo floor width: 213”
2” above floor width: 216”
Cargo Ramp
Length: 238”
Width: 216”
JALP
Notes: Added all text from reserves EN

## Slide 7
Height: Variable
  FS 347- 827: 148”
  FS 827- 937: 158”
  FS 937- 1165: 162”
JALP

## Slide 8
JALP
Notes: Planning ACL - up to 130,000 pounds
Higher ACLs are possible but only after coordination with your affiliated AMCU or in accordance with the Operation Order

## Slide 9
72,000
Total Wt.
170,900
Total Wt.
35,000
Total Wt.
40,000
Total Wt.
C-17 Cargo Compartment
FRONT
REAR
JALP
V

## Slide 10
COMPARTMENTS D,F, AND G
MAX single axle weight: 27,000lbs
Vehicle C/L must be within +/- 8in of aircraft C/L: 22,001-27,000lbs
Side by side loading allowed: 22,000lbs or less
COMPARTMENT E
MAX single axle weight: 36,000lbs
Vehicle C/L must be within +/- 8in of aircraft C/L: 27,001-36,000lbs
Side by side loading allowed: 27,000lbs or less
JALP
Single Axle Weight Limitations

## Slide 11
COMPARTMENTS | SIDE BY SIDE AXLE CHART | VEHICLE CENTERLINE MUST BE WITHIN +/-8 IN.OF AIRCRAFT C/L | MAX AXLE WT.
D/F/G | ≤22,000 LBS = D/F/G CHART | 22,001-27,000 LBS | 27,000 LBS
E | ≤27,000 LBS = E CHART | 27,001-36,000 LBS | 36,000 LBS
SINGLE AXLE LIMITATIONS

## Slide 12
AXLE LIMITATIONS
“8 FOOT ZONE”
JALP

## Slide 13
Applies to an 8 foot zone that extends 4 feet forward and 4 feet aft of the center of the “heaviest” single axle in that zone.
If two or more single axles fall within the 8 foot zone
  Axles will be treated as one axle.
  Total weight shall not exceed axle chart limits
Side By Side
Axle Limitations
JALP
14,000
6,000
6,000

## Slide 14
Compartments D/F/G
  Axle A weight determines the maximum allowable weight of Axle B
  Located in 1C-17A-9
  CANNOT BE USED TO LOAD OTHER AIRCRAFT!!!
SIDE BY SIDE
AXLE LIMITATIONS
JALP

## Slide 15
Compartment E
  Axle A weight determines the maximum allowable weight of Axle B
SIDE BY SIDE AXLE LIMITATIONS
JALP

## Slide 16
JALP
8 Foot Zone applies to vehicles loaded centerline
Use single axle compartment limitations
Axle Limitations Cont’d

## Slide 17
27,500
8,000
It must go in compartment “E” (FS 578-1074)
27,500 lb. axle must be within +/- 8” of aircraft centerline
Since 8,000 lb. axle is within 8’ zone; MUST add axles weights together
8,000 + 27,500 = 35,500 (Does not exceed 36,000 lb. limit)
Where can the 27,500 lbs axle go?
AXLE PROBLEM #1
JALP
Notes: Explain why the axle can not go in Compartments D/F/G

## Slide 18
AXLE PROBLEM #2
9000
9000
18,500
Can these vehicles be loaded into D compartment?
JALP

## Slide 19
C-17 Chart #1
27,000 Pound Axle Zone
FS 347 - 578, and FS 1074 - 1403
(Compartments D, F, and G)
24
24
22
22
20
20
18
18
16
16
14
14
12
12
10
10
8
8
6
6
4
4
2
2
0
0
Maximum Weight - Axle B ( x 1,000 Pounds)

## Slide 20
C-17 Chart #2
36,000 Pound Axle Zone
FS 578 - 1074
(Compartment E)
24
24
22
22
20
20
18
18
16
16
14
14
12
12
10
10
8
8
6
6
4
4
2
2
0
0
Maximum Weight - Axle B ( x 1,000 Pounds)
28
26
28
26

## Slide 21
AXLE PROBLEM #3
9000
7000
6000
JALP

## Slide 23
WHEELED/TRACKED VEHICLES
>65,000
8”
8”
JALP

## Slide 24
COMPARTMENTS | TRACKED VEHICLE WT | MAX AXLE WT NEXT TO TRACKED VEHICLE
D/F/G | ≤ 35,000 LBS | 16,000 LBS
D/F/G | 35,001-65,000 LBS | 11,000
COMPARTMENTS | TRACKED VEHICLE WT | MAX AXLE WT NEXT TO TRACKED VEHICLE
E | ≤ 35,000 LBS | 24,000 LBS
E | 35,001-65,000 LBS | 22,000 LBS
TRACKED VEHICLE LIMITATIONS
JALP
P
Notes: Compartments D,F,G (27,000 lb. zones)
Tracked vehicle weighing 35,000 lbs. or less, the max axle next to it can be 16,000 lbs. (8 foot zone restrictions still apply)
Tracked vehicle weighs 35,001 - 65,000 lbs., the max axle next to it can be 11,000 lbs. (8 foot zone restrictions still apply)
Compartment E (36,000 lb. zone)
Tracked vehicle weighing 35,000 lbs. or less, the max axle next to it can be 24,000 lbs. (8 foot zone restrictions still apply)
Tracked vehicle weighing 35,001 - 65,000 lbs., the max axle next to it can be 22,000 lbs. (8 foot zone restrictions still apply)

## Slide 25
PALLET CONSIDERATIONS
JALP

## Slide 26
All pallets can weigh 10,355 lbs per pallet position
Max height of 96”
JALP
Notes: All pallet positions can accommodate pal lets to a weight of 10,355 pounds
All pallet positions can accommodate pallets to a height of 96 inches

## Slide 27
1
5
2
6
7
11
9
4
3
13
8
15
14
16
12
10
17
18
LOGISTICAL RAIL SYSTEM (LOG)
JALP
Notes: The Logistics system can carry 18 pallets loaded on 88” width bias
14 pallets on the main floor and 4 pallets on the ramp
Can you have a chalk with 18 pallets loaded in this configuration?
(No, because 2 passengers are required per chalk)

## Slide 28
JALP

## Slide 29
1
5
2
6
7
11
9
4
3
8
10
AERIAL DELIVERY SYSTEM (ADS)
JALP
Notes: ADS system can carry 11 pallets loaded on 108” width bias
Allows for greater flexibility in the compromise between palletized cargo and troop/passenger seating

## Slide 30
JALP

## Slide 31
COMBINATION
LOG & ADS
JALP
Notes: Pallet restraint system allows for a mixture of both the logistics and aerial delivery systems
Allows for greater flexibility in the compromise between palletized cargo and troop/ passenger seating

## Slide 32
JALP
P

## Slide 33
PASSENGER CONSIDERATIONS
JALP

## Slide 34
JALP

## Slide 35
54
Permanently installed sidewall Seats
53
Available for use
>40
2 LM’s required
JALP

## Slide 36
102
101
Total seats (48 Optionally installed centerline seats)
Available for use
JALP
Notes: Centerline seats are setup in sets of 6 seats (3left/3right).
Centerline seats are not conducive to large cargo movements because 1 set can take up 3 to 4 pallet positions

## Slide 37
If bulk cargo and/or vehicles are loaded on the main cargo floor, sidewall seats adjacent to cargo extending +/- 85” of aircraft centerline will not be used
Passengers cannot be loaded next to logistics pallet positions
PASSENGERS
NEXT TO CARGO
JALP
L
Notes: If bulk cargo and/or vehicles are loaded on the main cargo floor, sidewall seats adjacent to cargo extending past +/- 85 inches of air craft centerline will not be used
If the vehicle width is greater than 85” wide, it must be offset L/R of centerline to utilize the seats for passengers. If it cannot be offset, passenger seats WILL NOT be used.
Explain to students this is a high failure item.
Optional: Explain line tool and how it can be used to give students a visual aid on the 85” line throughout the cargo compartment

## Slide 38
LOAD PLANNING CONFIGURATIONS
JALP

## Slide 39
Use STD-AL
AFI 11-2C-17 Vol. 3 Addenda A contains all configuration descriptions
JALP
Notes: ICODES has 15 different configurations for the C-17
AFI 11-2C-17 Vol. 3 Addenda A contains all configuration descriptions.

## Slide 40
  The C-17’s optimal CG is based on combined weight of aircraft + cargo.
    Less than 400K = 40% +/- 1% MAC
    400K to 425K = 39% +/- 1% MAC
    425K to 447K = 38% +/- 1% MAC
    MAC: A mathematical calculation that shows where the center of gravity is over the wing often expressed as a percentage on larger aircraft
JALP
V
Notes: Explain that for this class the weights meet the 400K-425K range and will use 39% +/- 1%

## Slide 41: QUESTIONS?
JALP

## Slide 42
Cargo Compartment Limitations
Pallet Considerations
Passenger Considerations
Load Planning Factors
SUMMARY
JALP