## Slide 3
C-5M CHARACTERISTICS

## Slide 4
Cargo Compartment Limitations
Pallet Considerations
Passenger Considerations
Load Planning Factors
OVERVIEW

## Slide 5
JALP
CARGO COMPARTMENT LIMITATIONS

## Slide 6: C-5M SUPER GALAXY
Inter-Theater Airlift (Strategic) of Outsized Cargo
Cargo Compartment Limitations
JALP

## Slide 7
Length of Cargo Floor- 1736”
MAX Width - 228”
MAX Height - 162”
USABLE CARGO DIMENSION
JALP

## Slide 8
Forward Ramp
FORWARD RAMP
Length – 122”
Width – 228”

## Slide 9
AFT RAMP
AFT RAMP
Length – 155”
Width – 228”
JALP

## Slide 10
Weight Considerations
Allowable Cabin Load (ACL)
JALP

## Slide 11
Rolling Stock Limitations/Weight Restrictions
3,600 lbs in any 20” length (FWD/AFT Ramps)
FS 395 – 517 FS 1971 - 2131
JALP

## Slide 12
20,000 lbs in any 40” length
FS 517 – 724 FS 1884 - 1971
Rolling Stock Limitations/Weight Restrictions
JALP

## Slide 13
36,000 lbs in any 40” length
FS 724 – 1458 FS 1518 - 1884
Rolling Stock Limitations/Weight Restrictions
JALP

## Slide 14
*25,000 lbs max weight
(Side-by-side/Multiple axles/Concentrated cargo)
FS 1458-1518
*Track Vehicles Excluded
Rolling Stock Limitations/Weight Restrictions
JALP

## Slide 15
114”
FWD Ladders
Height Restrictions
AFT Ladders
No Load Zone
Ref: T.O 1C-5M-9
JALP

## Slide 16
JALP
PALLET CONSIDERATIONS

## Slide 17
96”
96”
14” Aisle Ways
Forward Ramp Positions 1 & 2
Max WT of 7,500 lbs ea in 1 & 2
JALP

## Slide 18
10,355 lbs Max Pallet Wt
Main Cabin Floor Positions 3-34
JALP
Notes: Check -9 Sec 4 for position 33/34 restrictions for vertical CG.

## Slide 19
Max WT of 7,500 lbs ea in 35 & 36
14” Aisle Ways
70”
70”
Aft Ramp Positions 35 & 36
JALP

## Slide 20
JALP
PASSENGER CONSIDERATIONS

## Slide 21
Passenger Considerations
STEEP INCLINE/DECLINE STIARS
FACING AFT OF THE AIRCRAFT
-73 SEATS
JALP
Notes: Use picture from old slide

## Slide 22
TROOP COMPARTMENT
Separate Compartments
JALP

## Slide 23
ICODES CONFIGURATIONS
Ref: AFI 11-2C-5 Vol 3 Addenda A
Newer Engines/increased ACL
JALP
C-5 Galaxy
Vs
C-5M Super Galaxy

## Slide 24
JALP
LOAD PLANNING FACTORS

## Slide 25
38% (36% w/o pax & bags) +/- 1%
LOAD PLANNING FACTORS
OPTIMAL CG
EXAMPLE
Fuel Management & Optimization
JALP

## Slide 26
JALP
QUESTIONS?

## Slide 27
QUESTIONS?

## Slide 28
Cargo Compartment Limitations
Pallet Considerations
Passenger Considerations
Load Planning Factors
SUMMARY
JALP
Notes: Cargo Limitations
What is the ACL for the C-5M? (150,000)
What height are we limited to when loading cargo near the side walls? (114”)
Pallet Considerations
How tall can you build pallets on the AFT ramp of the C-5M? (70”)
What is the max pallet weight allowed on the FORWARD & AFT ramps? (7,500)
On the FORWARD & AFT ramp, how much inset do I need and why? (14” & ramp locking pins)
Passenger Considerations
How many passengers can fit in the Troop compartment? (73)
Are the crew compartment and troop compartment connected? (No)
Loading Planning Factors
What is the optimal CG range for the C-5M? (38% +/-1%)