## Slide 1: Hand and Arm Signals

## Slide 2: Start Engine or Prepare to Move (day)
At waist level, move the arm with fist in a circular motion
At waiste

## Slide 3: Halt or Stop (night)
Move a light horizontally back and forth several times across the path of approaching traffic
  Also used to stop engines

## Slide 4: Move Forward (day)
Face the vehicle, extend arms at chest height, palms facing upward.
Bend arms at elbow in upward motion.
Extend, again.
Repeat motion.

## Slide 5: Left Turn
Facing the vehicle, raise the right hand to chest height.
Extend arm horizontally at elbow, palm toward vehicle, and fingers extended.
Repeat motion.

## Slide 6: Right Turn (day)
Facing the vehicle, raise the left hand to chest height.
Extend arm horizontally at elbow, palm toward vehicle, fingers extended.
Repeat motion.

## Slide 7: Move in Reverse (day)
Face the vehicle, extend arms at chest height, palms facing downward.
Bend arms at elbow in upward motion.
Extend, again.
Repeat motion.

## Slide 8: Halt or Stop
Raise the hand upward to the full extent of the arm, with palm to the front
Hold that position until the signal is understood

## Slide 9: Stop Engine
Extend the arm parallel to the ground with hand open.
Move the arm across the body in a throat-cutting motion.