## Slide 1: Welcome to Unit Load Team Training

## Slide 2: Instructors
Chris Vanderlinde
Walter Brown
Eric Bundy

## Slide 3: Classroom Recommendations
DO
Take Notes
Pay Attention
Ask Questions
Reading is Recommended
DON’T
Operate Cell Phones
Use Tobacco Products
Have Open Containers on Tables

## Slide 4: Introduction
Rank / full name
Unit / MOS
Deployments
Rail Load/463L Pallet Packing background
Hobbies
Purpose for taking course

## Slide 5: Fort to Port Operations
Rail Operations

## Slide 6: References
ATP 3-35, Army Deployment and Redeployment
FM 4-01, Army Transportation Operations
FORSCOM/ARNG Reg 55-1, Unit Movement Planning
TM 55-2200-001-12, Application of Blocking, Bracing, Tie-down Materials
for Rail Transport
TEA PAM 55-19, Tie-Down Handbook for Rail Movements
TB 55-46-1, Standard Characteristics for Transportability of Military
Vehicles and Other Outsize/Overweight Equipment

## Slide 7: Surface Transportation
Used when equipment is non-roadable or beyond the unit’s organic lift capability
Rail requirements outlined in Annex N of Movement Order

## Slide 8: General Responsibilities
Rail loading/unloading
Rail car inspection
Restraining Material
Rail site preparation
TRANSPORTATION CORPS
US ARMY
U M & O Railroad
The deploying unit & installation both have planning and execution responsibilities for major rail activities

## Slide 9: Unit Responsibilities
Unit commander
  Overall responsibility to prepare unit for rail operations
Major unit responsibilities:
  Prepare rail movement plan (Unit Movement Plan, Annex N)
  Submit movement requirements to the ITO (OEL to UDL)
  Prepare equipment for rail movement
  Load railcars (under the technical supervision of the UMC)
UMO specific responsibilities:
  Appoint an OIC for the rail operation
  Designate safety officer
  Coordinate with DPW for blocking and bracing
  Provide trained load teams
  Provide all required HAZMAT documentation to ITO
  Ensure vehicles are properly prepared/configured
    Remove canvas and bows
    Secure moving vehicle parts
    Pack, crate, band, and block & brace secondary loads
    Use SDDCTEA Pam 55-19

## Slide 10: Unit Responsibilities Cont.
Coordinate logistical support for railhead ops
    Lighting, latrines, mess, and medical
Ensure tie-down teams have proper equipment
Stage equipment
Ensure sufficient numbers of cars are spotted
Inspect rail cars
Conduct safety briefings
Prepare rail cars for loading
Load and tie-down equipment on rail cars

## Slide 11: ITO Responsibilities
Order rail cars based on deploying unit’s requirements
Compute railcars based on shipping configuration of equipment
(requires accurate UDL)
Prepare Government Bill of Lading
Official liaison with SDDC and railway agent
Designate installation load-out staging area
Joint Inspection of railroad representative prior to loading

## Slide 12: ITO Responsibilities cont
Provide technical advice to units on BBPCT (Blocking, Bracing, Packing, Crating, and Tie-down)
Provide spanners as required
Notify unit on schedule type and quantity of railcars (cognizant of
scheduled arrival date at POE - as listed in TPFDD (Time Phased Force Deployment Data))
Publish/maintain rail loading schedule according to movement order
Joint inspection of loaded railcars with railway agent to ensure
compliance with Army Regulations, AAR loading rules, and/or HN rules
Provide DD Form 2890, if necessary, for HAZMAT

## Slide 13: SDDC Responsibilities
Obtain railcars and routing information from carrier supporting the move
Advises ITO of route restrictions (height / weight)
Units may request help through the SDDC Operations Center; Scott AFB, IL
    Unit Movement Teams from Deployment Support Brigades (USAR) are available for dispatch to support unit preparation for movement
    Request SDDC assistance through the UMC/ITO

## Slide 14: Rail Carrier Responsibilities
Joint inspection with ITO before cars positioned at loading ramp
Final approving authority for accepting the rail loads
Inspection following railcar loading to ensure that loaded railcars comply
with AAR rules
Assumes responsibility of cargo after final inspection

## Slide 15: Railcar Requirements
Based upon the deploying unit’s requirements (UDL)
Rail cars are obtained by ITO in the types and quantities required
Deployment may be by commercial or ‘DODX’ railcars
There are several types of railcars used for military exercises and
deployments depending on the type of cargo being moved:
    Flat Cars
    Box Cars
    Gondola
    Hopper Cars
    Tank Cars
    Caboose

## Slide 16: Official Railway Equipment Register
Used to determine type of rail cars
needed
Lists the capacity/dimensions of each
type of railcar
Excerpts for commercial & DODX
railcars contained in
TM 55-2200-001-12

## Slide 17: Association of American Railways (AAR)
Excerpts of AAR Rules contained in
TM 55-2200-001-12
Contains tie-down information for military vehicles & equipment
Abide by host nation rail rules and regulations OCONUS

## Slide 18: TM 55-2200-001-12
Appendix G contains information on commercial special-purpose railcars
Appendix H-1 contains the DODX table used to determine the types of DODX rail cars needed and their associated capacity and dimensions

## Slide 19
On
Learning

## Slide 20
On
Learning
Question 1: Who is responsible for obtaining rail cars for the deploying unit?
Answer 1: The Installation Transportation Office - ITO

## Slide 21
On
Learning
Question 2: When railcars arrive on site,
who is responsible for inspecting the railcars prior to accepting the cars from the rail carrier?
Answer 2: The ITO is responsible for the initial inspection prior to accepting the railcars

## Slide 22
On
Learning
Question 3: Who is responsible for providing the deploying unit with spanners for rail loading operations?
Answer 3: The Installation Transportation Office - ITO

## Slide 23
On
Learning
Question 4: What established rules govern all rail movements in CONUS?
Answer 4: Association of American Railways (AAR) rules

## Slide 24: Summary
Responsibilities
  Unit
  ITO
  SDDC
  Rail Carrier
Official Railway Equipment Register
TM 55-2200-001-12

## Slide 25: Combination Yard Layout
Loading Ramps
Main Track
= Switch
Siding # 1
Siding # 2
Siding # 3
Siding # 4
Siding # 5
Siding # 6
Siding # 7

## Slide 26: Types of Loading Ramps
Fixed Concrete Ramp
Portable Ramp

## Slide 27: Hank’s Yard at JBLE

## Slide 28: DFRIF
Flatcars:
General Purpose 1477
Special Purpose 139
Tank cars:
General Purpose 375
Special Purpose 18
Boxcars:
Special Purpose 30
Refrigerated 9
Misc cars:
Escort Cabooses 6
Guard Cars 5
Spec Lease 11
Total DODX: 2070
Defense Freight Rail Interchange Fleet
Mainly used for over-dimensional equipment or to meet deployment time constraints
Controlled by SDDC
Pre-positioned at PPP installations to meet time constraints

## Slide 29: Flatcars
Ideal for transporting military cargo and vehicles
Equipment may be carried on DOD or common carrier flatcars
Tie-down information
on side of railcar

## Slide 30: Multi-Level Flatcars
May be open or closed
Taller vehicles on upper level
Ramps used to load upper levels

## Slide 31: TOFC Flatcars
Trailer on Flatcar

## Slide 32: Types of MHE / CHE

## Slide 33: Boxcars
U.S. Boxcars in domestic service have a capacity of about 100k lbs or over 3900 cu. ft.
Ideal for commodities requiring protection from weather or susceptible to pilferage, such as:
  Foodstuffs
  Medicines
  Electronics
  Spare parts
  Ammunition

## Slide 34: Gondola Cars
Gondola cars sides prevent bulk loads from shifting

## Slide 35: Switch Engines
Used to switch rail cars in and out of a loading area

## Slide 36: Line Haul Locomotives
Used to transport cargo over long distances

## Slide 37: Caboose
Not used on civilian trains
Only used when escorts are required for transporting classified or sensitive items

## Slide 38
On
Learning

## Slide 39
On
Learning
Question 1: What enhanced rail deployment capability does the Defense Freight Rail Interchange Fleet (DFRIF) provide?
Answer 1: Pre-positioning of railcars at selected installations provides flexibility to quickly load military equipment for deployment operations.

## Slide 40
On
Learning
Question 2: What type of railcar is ideal for
transporting wheeled and tracked vehicles
and oversized equipment?
Answer 2: Flat Cars

## Slide 41: Summary
Rail Yard Layout
Types of Railcars
Defense Freight Rail Interchange Fleet (DFRIF)
  DODX Railcars

## Slide 42: Rail Loading Requirements and Procedures

## Slide 43: Equipment Prep for Rail Movement
The deploying unit is responsible for preparing its vehicles and
equipment for rail movement
      Cleaning
      Configuration
      Documentation

## Slide 44: General Guidance
Don’t carry ammunition and fuel as secondary cargo together
on any vehicle during rail movement
Place warning placards on all sides of hazardous cargo loads
Load as much unit equipment as possible in organic vehicles
Secure equipment loads properly
Lock/seal sensitive materials in approved security containers:
      Arms
      Ammo
      Explosives

## Slide 45: Vehicle Prep for Rail Movement
Vehicle Preparation Requirements:
  All lifting and tie-down shackles attached to vehicles
  Fuel tanks no more than 3/4 full
  Canvas and bows removed or banded
  Check inflation and condition of tires
    New series vehicles (e.g. PLS, HET, HEMTT):
        Windows remain up to prevent potential damage to electronic transmission
        and central tire inflation systems
        Protect with plywood, cardboard, or double layer of bubble wrap

## Slide 46: Vehicle Prep Cont.
Reduce vehicle configuration based on movement order
Secure any materials or equipment
Bands must be approved by AAR
Ensure hood latches are functional and secure

## Slide 47: Blocking & Bracing Materials
B & B references contained in both TM 55-2200-001-12 and SDDCTEA Pam 55-19
May be reused if serviceable

## Slide 48: Rail Site Facilities
Command and control
Medical support
Warming Tent
Latrine facilities
Lighting
Messing

## Slide 49: Rail Site Facilities
Rail site must be clean and free of debris
Ensure spanners are available
Ensure MHE is on site for equipment requiring support

## Slide 50: Safety Requirements
Appoint Safety OIC or NCOIC to conduct risk assessment before loading
Qualified, properly equipped medical personnel on site
Brief soldiers on safety procedures prior to loading:
    Must wear leather gloves & hard hats/helmets
    Goggles & safety boots recommended
    Night loading: Prepare adequate lighting and ensure personnel have reflector vests and flashlights
    Do not step or walk on the rails
    Never walk backwards on rail cars
    Do not run on, jump between, or jump off of railcars use steps provided
    Do not crawl under or walk between railcars
    All vehicles moving on railcar must have 1 car guide (on the rail car in front of the vehicle) and 2 side guides (on the ground on each side of the vehicle)
    Car guide gives instructions to the vehicle driver; side guides advise car guide of how close the vehicle is to the edge of the railcar

## Slide 51: Safety Requirements Cont.
Car guide should stay one railcar ahead of vehicle being guided and be in clear view of the operator at all times
If vehicle is already on railcar, assume a secure and observable position on or beside the parked vehicle so that you cannot be pinned between the moving and parked vehicles
Car guides must use uniform hand signals (drivers must understand these signals)

## Slide 52: Safety Requirements Cont.
Ensure spanners are properly aligned and secured before a vehicle drivers over them
Do not stand beside spanners when vehicle drives over them
Reduced speed is used when driving vehicles onto railcars
Personnel must stay clear of main track and railcars when vehicles are moving on them (except designated guides)
No sleeping in or around rail cars
Be aware of overhead electric power lines
Display a blue flag on the track behind the
last car being loaded so other trains will
not approach

## Slide 53: Inspection of Railcars
Inspect prior to being positioned at final loading locations
Purpose is to determine the cars suitability for intended equipment/vehicle loads
After railcars are accepted, military accepts full responsibility to comply with AAR rules
ITO and railway agent perform joint inspection of railcars prior to loading equipment
Checks include:
Doors on closed cars open and close and interior is free of debris
Open car decks free of residue and old B & B materials
Chains are present and serviceable on chain equipped rail cars

## Slide 54
CONUS General Rail Loading
Rules
Front of Train

## Slide 55: AAR Loading Rules
The AAR makes no provision to protect cargo from the elements or other forms of damage
Loading rules apply to both the railroad and the ITO/Unit
Railcar load and weight limits must not be exceeded

## Slide 56: AAR Loading Rules Cont.
½ the load limit of the railcar must not be exceeded on any axle truck
Balance load evenly on car
For large/heavy items not covered by rules, load largest dimensions and
heaviest weight on floor to prevent tipping
Items with a high center of balance (C/B) must be secured to prevent
tipping while in transit
Loads must be adequately secured to railcars
Railcars must be suitable for safe transportation of load
Load must not exceed width/height restrictions of route

## Slide 57: HAZMAT
IAW Title 49, CFR and DTR Part II
Consider exclusions, marking, and placarding
If exemption required, SDDC will request from carrier
Carrier provides certificates needed for Class 1 explosives
Rail cars used for shipment of explosives must be properly sealed
with Army approved seal

## Slide 58: Sensitive / Classified Material
When shipping sensitive or classified material by rail, commanders may
be required to provide guards/escorts
Cargo guards/escorts maintain surveillance of military equipment during
the journey and notify railroad personnel of any problems
Escort supervisor given copy itinerary (interchange points, stops, etc.)
Escorts given portable radios and safety/ROE briefs prior to departure

## Slide 59: Escort / Guard Duties
Conduct cargo checks 1 - 2 hours before departure
Do cargo checks when train stops for 30 minutes or more
(check for shifting, tampering, missing seals, & missing/damaged cargo)
During stops, guards stagger along both sides of train
Report issues that could delay shipments to SDDC immediately

## Slide 60: Preparation of Railcars
Deploying unit checks tie-downs and positions them on railcar to avoid
repositioning chains after vehicles are loaded
Unused chains placed in channels to prevent damage
Ensure railcar brakes are applied and wheels chocked to prevent railcars
shifting while loading
* Leave 6” clearance around brake wheel

## Slide 61: Vehicle and Equipment Loading
Prior to loading, stage vehicles in order of loading
Most common and expeditious method for loading vehicles on flatcars is
the “circus” method:
  Flatcars and spanners used as roadbed
  Spanners adjusted as required for each vehicle type
  All vehicles loaded on rearmost car, then moved forward to assigned locations
Prior to loading the vehicle onto railcar, all personnel with the exception of the driver must dismount vehicle
Rail guide should be one car ahead of vehicle or positioned not to be caught between vehicles

## Slide 62: Loading Cont.
Ensure spanners are properly positioned & capable of supporting the heaviest load anticipated
At least 12” of spanner should overlap the rail car deck
Most track vehicles don’t require spanners between rail cars
When loading vehicle between railcars of uneven deck heights, place dunnage under the spanner to prevent it from slipping
Ramp
Spanner

## Slide 63: Loading Cont.
When driving on spanners, maintain a constant speed
Avoid jamming on brakes or reversing

## Slide 64: Vehicle Spacing
Vehicles require a minimum of 10” of space between vehicles
For rail cars with top mounted brake wheels, ensure there is sufficient space for operation
Correct spacing
Incorrect spacing
* See pg. 2 of TEA PAM 55-19

## Slide 65: Tie down Procedures
When securing vehicles use these techniques:
Inspect chain assemblies and
components for damage, missing
parts, and proper operation
Apply chains in pairs and equal
numbers front and rear
Consult TEA PAM 55-19 for cargo
tie down requirements
Secure chain through tie-down points
at 45o angle

## Slide 66: Loading & Tie down Checklist
Checklists should be distributed to the loading teams and should
contain the following:

## Slide 67: TEA PAM 55-19
App A: Trucks and Trailers
App B: Tracked and Wheeled Armored Vehicles
App C: MHE, Construction Equipment, & Non-Vehicles
Checklists for tie-down procedures on page 34

## Slide 68: Chain Tie-down Illustration Trucks up to 80,000 lbs
Alloy Steel chain with a thickness of 3/8” or 1/2”
TEA PAM 55-19
  Appendix A
  Page A-2

## Slide 69: Final Inspection
Final inspection is made after loading railcars to ensure that the contents are loaded and secured in compliance with AAR
The rail representative is the final approving authority for accepting rail loads

## Slide 70: Unloading
Railcars off-loaded promptly at destination for return and to avoid demurrage or detention charges (usually within 48 hrs)
Units must remove BBPCT materials from unloaded cars before releasing to carrier

## Slide 71
On
Learning

## Slide 72: On Learning
Question 1: What is the procedure used in the “circus loading” of unit equipment on railcars?
Answer 1: The “circus loading” method uses flatcars as a roadbed with spanners between the railcars. Vehicles are loaded from the rear most railcar and then moved forward to their assigned locations.

## Slide 73: On Learning
Question 2: What is the minimum amount of space that must be maintained between vehicles that are secured to the railcar deck?
Answer 2: AAR rules require a minimum of 10 inches between vehicles.

## Slide 74: On Learning
Question 3: What reference provides a checklist for loading and tying down unit equipment on railcars?
Answer 3: SDDC TEA Pam 55-19, Tiedown Handbook for Rail Movements

## Slide 75: Summary
Preparing for Rail Movement
Rail Site Facilities
Safety Requirements
Loading/Unloading Procedures

## Slide 76
Questions?

## Slide 77
Installation
Transportation
Office

## Slide 78
Slip Hook

## Slide 79
Grab Hook

## Slide 80
Adjustable
Double
Grab
Hook

## Slide 81
Lacing a Grab Hook with Chain

## Slide 82
Claw

## Slide 83
Donut Ring

## Slide 85
Round Pin Anchor Shackle

## Slide 87
Trailer Shackle

## Slide 88
Tie Down
Absorber

## Slide 89
Compression Unit
Jamnut
Eye Bolt

## Slide 90
Air Force Pallet Hooks

## Slide 91
Pipe Wrench

## Slide 92
Wally Bar

## Slide 93
Sledge Hammer

## Slide 94
Crow Bar

## Slide 96
Tie Down
Mock Up