## Slide 1
M249 WRITTEN PE (DECEMBER 2017)
1. The M249 is ______________ operated?
a. Blowback b. Recoil c. Gas d. Manually
2. The armorer can replace which part?
a. Safety b. Grip assembly c. Sear spring d. None of these
3. The M249 machine gun is fired from the ___________ bolt position?
a. Open b. Closed c. Centered d. None of the above
4. If the safety fails to slide properly after cleaning, what corrective action would you take?
a. Replace safety b. Send to depot c. Send to field maintenance d. None of the above
5. A damaged cartridge guide could cause a failure to?
a. Feed b. Extract c. Fire d. None of the above

## Slide 2
M249 WRITTEN PE (DECEMBER 2017)
1. The M249 is ______________ operated?
a. Blowback b. Recoil c. Gas d. Manually
2. The armorer can replace which part?
a. Safety b. Grip assembly c. Sear spring d. None of these
3. The M249 machine gun is fired from the ___________ bolt position?
a. Open b. Closed c. Centered d. None of the above
4. If the safety fails to slide properly after cleaning, what corrective action would you take?
a. Replace safety b. Send to depot c. Send to field maintenance d. None of the above
5. A damaged cartridge guide could cause a failure to?
a. Feed b. Extract c. Fire d. None of the above

## Slide 3
M249 WRITTEN PE (DECEMBER 2017)
1. The M249 is ______________ operated?
a. Blowback b. Recoil c. Gas d. Manually
2. The armorer can replace which part?
a. Safety b. Grip assembly c. Sear spring d. None of these
3. The M249 machine gun is fired from the ___________ bolt position?
a. Open b. Closed c. Centered d. None of the above
4. If the safety fails to slide properly after cleaning, what corrective action would you take?
a. Replace safety b. Send to depot c. Send to field maintenance d. None of the above
5. A damaged cartridge guide could cause a failure to?
a. Feed b. Extract c. Fire d. None of the above

## Slide 4
M249 WRITTEN PE (DECEMBER 2017)
1. The M249 is ______________ operated?
a. Blowback b. Recoil c. Gas d. Manually
2. The armorer can replace which part?
a. Safety b. Grip assembly c. Sear spring d. None of these
3. The M249 machine gun is fired from the ___________ bolt position?
a. Open b. Closed c. Centered d. None of the above
4. If the safety fails to slide properly after cleaning, what corrective action would you take?
a. Replace safety b. Send to depot c. Send to field maintenance d. None of the above
5. A damaged cartridge guide could cause a failure to?
a. Feed b. Extract c. Fire d. None of the above

## Slide 5
M249 WRITTEN PE (DECEMBER 2017)
1. The M249 is ______________ operated?
a. Blowback b. Recoil c. Gas d. Manually
2. The armorer can replace which part?
a. Safety b. Grip assembly c. Sear spring d. None of these
3. The M249 machine gun is fired from the ___________ bolt position?
a. Open b. Closed c. Centered d. None of the above
4. If the safety fails to slide properly after cleaning, what corrective action would you take?
a. Replace safety b. Send to depot c. Send to field maintenance d. None of the above
5. A damaged cartridge guide could cause a failure to?
a. Feed b. Extract c. Fire d. None of the above

## Slide 6
M249 WRITTEN PE (DECEMBER 2017)
What is the corrective action for a plugged gas regulator (mono-block)?
a. (O) b. (H) c. (F) d. (D)
A failure to extract could be caused by?
a. Ejector worn b. Insufficient gas pressure c. Loose tower d. Firing pin damaged
8. A defective sear could cause a failure to?
a. Lock b. Feed c. Cock d. Unlock
The M249 machine gun
a. Is a semi-automatic weapon
b. Is belt or magazine fed
c. Fires from the close bolt position
d. Is recoil operated
The tripping lever is attached to the?
a. Sear b. Bolt c. Safety d. None of the above

## Slide 7
M249 WRITTEN PE (DECEMBER 2017)
What is the corrective action for a plugged gas regulator (mono-block)?
a. (O) b. (H) c. (F) d. (D)
A failure to extract could be caused by?
a. Ejector worn b. Insufficient gas pressure c. Loose tower d. Firing pin damaged
8. A defective sear could cause a failure to?
a. Lock b. Feed c. Cock d. Unlock
The M249 machine gun
a. Is a semi-automatic weapon
b. Is belt or magazine fed
c. Fires from the close bolt position
d. Is recoil operated
The tripping lever is attached to the?
a. Sear b. Bolt c. Safety d. None of the above

## Slide 8
M249 WRITTEN PE (DECEMBER 2017)
What is the corrective action for a plugged gas regulator (mono-block)?
a. (O) b. (H) c. (F) d. (D)
A failure to extract could be caused by?
a. Ejector worn b. Insufficient gas pressure c. Loose tower d. Firing pin damaged
8. A defective sear could cause a failure to?
a. Lock b. Feed c. Cock d. Unlock
The M249 machine gun
a. Is a semi-automatic weapon
b. Is belt or magazine fed
c. Fires from the close bolt position
d. Is recoil operated
The tripping lever is attached to the?
a. Sear b. Bolt c. Safety d. None of the above

## Slide 9
M249 WRITTEN PE (DECEMBER 2017)
What is the corrective action for a plugged gas regulator (mono-block)?
a. (O) b. (H) c. (F) d. (D)
A failure to extract could be caused by?
a. Ejector worn b. Insufficient gas pressure c. Loose tower d. Firing pin damaged
8. A defective sear could cause a failure to?
a. Lock b. Feed c. Cock d. Unlock
The M249 machine gun
a. Is a semi-automatic weapon
b. Is belt or magazine fed
c. Fires from the close bolt position
d. Is recoil operated
The tripping lever is attached to the?
a. Sear b. Bolt c. Safety d. None of the above

## Slide 10
M249 WRITTEN PE (DECEMBER 2017)
What is the corrective action for a plugged gas regulator (mono-block)?
a. (O) b. (H) c. (F) d. (D)
A failure to extract could be caused by?
a. Ejector worn b. Insufficient gas pressure c. Loose tower d. Firing pin damaged
8. A defective sear could cause a failure to?
a. Lock b. Feed c. Cock d. Unlock
The M249 machine gun
a. Is a semi-automatic weapon
b. Is belt or magazine fed
c. Fires from the close bolt position
d. Is recoil operated
The tripping lever is attached to the?
a. Sear b. Bolt c. Safety d. None of the above

## Slide 11
M249 WRITTEN PE (DECEMBER 2017)
What is the corrective action for a plugged gas regulator (mono-block)?
a. (O) b. (H) c. (F) d. (D)
A failure to extract could be caused by?
a. Ejector worn b. Insufficient gas pressure c. Loose tower d. Firing pin damaged
8. A defective sear could cause a failure to?
a. Lock b. Feed c. Cock d. Unlock
The M249 machine gun
a. Is a semi-automatic weapon
b. Is belt or magazine fed
c. Fires from the close bolt position
d. Is recoil operated
The tripping lever is attached to the?
a. Sear b. Bolt c. Safety d. None of the above

## Slide 12
M249 WRITTEN PE (DECEMBER 2017)
11. A failure to charge could be caused by?
a. Frame trigger c. Bent arm on the cocking handle
b. Shoulder rest d. None of these
12. The first check in a failure to chamber?
a. Check for defective buffer c. Check for spent cartridge
b. Charging handle d. None of these
13. A failure to fire could be caused by?
a. Firing pin tip damaged c. Bolt jammed
b. Feed mechanism is sticking d. All of these
The first step in troubleshooting a failure to fire is?
a. Check for improperly installed firing pin b. Check for loose gas collar
c. Check for broken firing pin d. None of the above
A damaged sear will result in a failure to?
a. Eject. b. Lock c. Cock. d. Chamber.

## Slide 13
M249 WRITTEN PE (DECEMBER 2017)
11. A failure to charge could be caused by?
a. Frame trigger c. Bent arm on the cocking handle
b. Shoulder rest d. None of these
12. The first check in a failure to chamber?
a. Check for defective buffer c. Check for spent cartridge
b. Charging handle d. None of these
13. A failure to fire could be caused by?
a. Firing pin tip damaged c. Bolt jammed
b. Feed mechanism is sticking d. All of these
The first step in troubleshooting a failure to fire is?
a. Check for improperly installed firing pin b. Check for loose gas collar
c. Check for broken firing pin d. None of the above
A damaged sear will result in a failure to?
a. Eject. b. Lock c. Cock. d. Chamber.

## Slide 14
M249 WRITTEN PE (DECEMBER 2017)
11. A failure to charge could be caused by?
a. Frame trigger c. Bent arm on the cocking handle
b. Shoulder rest d. None of these
12. The first check in a failure to chamber?
a. Check for defective buffer c. Check for spent cartridge
b. Charging handle d. None of these
13. A failure to fire could be caused by?
a. Firing pin tip damaged c. Bolt jammed
b. Feed mechanism is sticking d. All of these
The first step in troubleshooting a failure to fire is?
a. Check for improperly installed firing pin b. Check for loose gas collar
c. Check for broken firing pin d. None of the above
A damaged sear will result in a failure to?
a. Eject. b. Lock c. Cock. d. Chamber.

## Slide 15
M249 WRITTEN PE (DECEMBER 2017)
11. A failure to charge could be caused by?
a. Frame trigger c. Bent arm on the cocking handle
b. Shoulder rest d. None of these
12. The first check in a failure to chamber?
a. Check for defective buffer c. Check for spent cartridge
b. Charging handle d. None of these
13. A failure to fire could be caused by?
a. Firing pin tip damaged c. Bolt jammed
b. Feed mechanism is sticking d. All of these
The first step in troubleshooting a failure to fire is?
a. Check for improperly installed firing pin b. Check for loose gas collar
c. Check for broken firing pin d. None of the above
A damaged sear will result in a failure to?
a. Eject. b. Lock c. Cock. d. Chamber.

## Slide 16
M249 WRITTEN PE (DECEMBER 2017)
11. A failure to charge could be caused by?
a. Frame trigger c. Bent arm on the cocking handle
b. Shoulder rest d. None of these
12. The first check in a failure to chamber?
a. Check for defective buffer c. Check for spent cartridge
b. Charging handle d. None of these
13. A failure to fire could be caused by?
a. Firing pin tip damaged c. Bolt jammed
b. Feed mechanism is sticking d. All of these
The first step in troubleshooting a failure to fire is?
a. Check for improperly installed firing pin b. Check for loose gas collar
c. Check for broken firing pin d. None of the above
A damaged sear will result in a failure to?
a. Eject. b. Lock c. Cock. d. Chamber.

## Slide 17
M249 WRITTEN PE (DECEMBER 2017)
11. A failure to charge could be caused by?
a. Frame trigger c. Bent arm on the cocking handle
b. Shoulder rest d. None of these
12. The first check in a failure to chamber?
a. Check for defective buffer c. Check for spent cartridge
b. Charging handle d. None of these
13. A failure to fire could be caused by?
a. Firing pin tip damaged c. Bolt jammed
b. Feed mechanism is sticking d. All of these
The first step in troubleshooting a failure to fire is?
a. Check for improperly installed firing pin b. Check for loose gas collar
c. Check for broken firing pin d. None of the above
A damaged sear will result in a failure to?
a. Eject. b. Lock c. Cock. d. Chamber.

## Slide 18
M249 WRITTEN PE (DECEMBER 2017)
Extraction begins while the unlocking cycle in going on?
a. True
b. False
Which part of the gas system should never be lubricated?
a. Piston b. Regulator c. Gas tube d. All of the above
Where are the cleaning patches and CLP stored on the weapon?
_______________________
PMCS for the M249 machine gun are scheduled on a __________ basis?
a. Daily b. Weekly c. Quarterly d. Monthly
A broken driving spring could cause a failure to feed, what other cycle of function could it cause a failure in?
a. Cock b. Fire c. Unlock d. Chamber

## Slide 19
M249 WRITTEN PE (DECEMBER 2017)
Extraction begins while the unlocking cycle in going on?
a. True
b. False
Which part of the gas system should never be lubricated?
a. Piston b. Regulator c. Gas tube d. All of the above
Where are the cleaning patches and CLP stored on the weapon?
_______________________
PMCS for the M249 machine gun are scheduled on a __________ basis?
a. Daily b. Weekly c. Quarterly d. Monthly
A broken driving spring could cause a failure to feed, what other cycle of function could it cause a failure in?
a. Cock b. Fire c. Unlock d. Chamber

## Slide 20
M249 WRITTEN PE (DECEMBER 2017)
Extraction begins while the unlocking cycle in going on?
a. True
b. False
Which part of the gas system should never be lubricated?
a. Piston b. Regulator c. Gas tube d. All of the above
Where are the cleaning patches and CLP stored on the weapon?
_______________________
PMCS for the M249 machine gun are scheduled on a __________ basis?
a. Daily b. Weekly c. Quarterly d. Monthly
A broken driving spring could cause a failure to feed, what other cycle of function could it cause a failure in?
a. Cock b. Fire c. Unlock d. Chamber

## Slide 21
M249 WRITTEN PE (DECEMBER 2017)
Extraction begins while the unlocking cycle in going on?
a. True
b. False
Which part of the gas system should never be lubricated?
a. Piston b. Regulator c. Gas tube d. All of the above
Where are the cleaning patches and CLP stored on the weapon?
PISTOL GRIP
PMCS for the M249 machine gun are scheduled on a __________ basis?
a. Daily b. Weekly c. Quarterly d. Monthly
A broken driving spring could cause a failure to feed, what other cycle of function could it cause a failure in?
a. Cock b. Fire c. Unlock d. Chamber

## Slide 22
M249 WRITTEN PE (DECEMBER 2017)
Extraction begins while the unlocking cycle in going on?
a. True
b. False
Which part of the gas system should never be lubricated?
a. Piston b. Regulator c. Gas tube d. All of the above
Where are the cleaning patches and CLP stored on the weapon?
PISTOL GRIP
PMCS for the M249 machine gun are scheduled on a __________ basis?
a. Daily b. Weekly c. Quarterly d. Monthly
A broken driving spring could cause a failure to feed, what other cycle of function could it cause a failure in?
a. Cock b. Fire c. Unlock d. Chamber

## Slide 23
M249 WRITTEN PE (DECEMBER 2017)
Extraction begins while the unlocking cycle in going on?
a. True
b. False
Which part of the gas system should never be lubricated?
a. Piston b. Regulator c. Gas tube d. All of the above
Where are the cleaning patches and CLP stored on the weapon?
PISTOL GRIP
PMCS for the M249 machine gun are scheduled on a __________ basis?
a. Daily b. Weekly c. Quarterly d. Monthly
A broken driving spring could cause a failure to feed, what other cycle of function could it cause a failure in?
a. Cock b. Fire c. Unlock d. Chamber

## Slide 24
M249 WRITTEN PE (DECEMBER 2017)
21. What is the status symbol for a chipped ejector tip when the fault is listed on the DA Form 5988-E?
___________
22. What is the difference between the old and new style barrels?
_________________
23. All barrels should be gauged and have a 100% technical inspection how often?
______________________
24. What does the SMR code of XA mean? ____________________
_____________________________________________________
25. What three parts of the trigger mechanism, if defective, could cause a failure to cock?
___________________, ________________, and ________________

## Slide 25
M249 WRITTEN PE (DECEMBER 2017)
21. What is the status symbol for a chipped ejector tip when the fault is listed on the DA Form 5988-E?
X
22. What is the difference between the old and new style barrels?
_________________
23. All barrels should be gauged and have a 100% technical inspection how often?
______________________
24. What does the SMR code of XA mean? ____________________
_____________________________________________________
25. What three parts of the trigger mechanism, if defective, could cause a failure to cock?
___________________, ________________, and ________________

## Slide 26
M249 WRITTEN PE (DECEMBER 2017)
21. What is the status symbol for a chipped ejector tip when the fault is listed on the DA Form 5988-E?
X
22. What is the difference between the old and new style barrels?
MONO BLOCK
23. All barrels should be gauged and have a 100% technical inspection how often?
______________________
24. What does the SMR code of XA mean? ____________________
_____________________________________________________
25. What three parts of the trigger mechanism, if defective, could cause a failure to cock?
___________________, ________________, and ________________

## Slide 27
M249 WRITTEN PE (DECEMBER 2017)
21. What is the status symbol for a chipped ejector tip when the fault is listed on the DA Form 5988-E?
X
22. What is the difference between the old and new style barrels?
MONO BLOCK
23. All barrels should be gauged and have a 100% technical inspection how often?
ANNUALY
24. What does the SMR code of XA mean? ____________________
_____________________________________________________
25. What three parts of the trigger mechanism, if defective, could cause a failure to cock?
___________________, ________________, and ________________

## Slide 28
M249 WRITTEN PE (DECEMBER 2017)
21. What is the status symbol for a chipped ejector tip when the fault is listed on the DA Form 5988-E?
X
22. What is the difference between the old and new style barrels?
MONO BLOCK
23. All barrels should be gauged and have a 100% technical inspection how often?
ANNUALY
What does the SMR code of XA mean?
DO NOT REQUISITION
25. What three parts of the trigger mechanism, if defective, could cause a failure to cock?
___________________, ________________, and ________________

## Slide 29
M249 WRITTEN PE (DECEMBER 2017)
21. What is the status symbol for a chipped ejector tip when the fault is listed on the DA Form 5988-E?
X
22. What is the difference between the old and new style barrels?
MONO BLOCK
23. All barrels should be gauged and have a 100% technical inspection how often?
ANNUALY
What does the SMR code of XA mean?
DO NOT REQUISITION
25. What three parts of the trigger mechanism, if defective, could cause a failure to cock?
SEAR, SEAR SPRING AND TRIPING LEVER