## Slide 1: M17 PRACTICAL EXERCISE
1. During which cycle of function/operation on the M17 does pressing the trigger release the striker pin?
Firing b. Unlocking c. Extraction d. Ejection
2. During which cycle of function/operation on the M17 does the barrel unlocks from the slide and stops its rearward movement?
Firing b. Unlocking c. Feeding d. Chambering
3. During which cycle of function/operation on the M17 is the empty cartridge pulled from the chamber of the stationary barrel as the slide continues its rearward travel?
Firing b. Unlocking c. Extraction d. Ejection

## Slide 2: M17 PRACTICAL EXERCISE
1. During which cycle of function/operation on the M17 does pressing the trigger release the striker pin?
Firing b. Unlocking c. Extraction d. Ejection
2. During which cycle of function/operation on the M17 does the barrel unlocks from the slide and stops its rearward movement?
Firing b. Unlocking c. Feeding d. Chambering
3. During which cycle of function/operation on the M17 is the empty cartridge pulled from the chamber of the stationary barrel as the slide continues its rearward travel?
Firing b. Unlocking c. Extraction d. Ejection

## Slide 3: M17 PRACTICAL EXERCISE
1. During which cycle of function/operation on the M17 does pressing the trigger release the striker pin?
Firing b. Unlocking c. Extraction d. Ejection
2. During which cycle of function/operation on the M17 does the barrel unlocks from the slide and stops its rearward movement?
Firing b. Unlocking c. Feeding d. Chambering
3. During which cycle of function/operation on the M17 is the empty cartridge pulled from the chamber of the stationary barrel as the slide continues its rearward travel?
Firing b. Unlocking c. Extraction d. Ejection

## Slide 4: M17 PRACTICAL EXERCISE
1. During which cycle of function/operation on the M17 does pressing the trigger release the striker pin?
Firing b. Unlocking c. Extraction d. Ejection
2. During which cycle of function/operation on the M17 does the barrel unlocks from the slide and stops its rearward movement?
Firing b. Unlocking c. Feeding d. Chambering
3. During which cycle of function/operation on the M17 is the empty cartridge pulled from the chamber of the stationary barrel as the slide continues its rearward travel?
Firing b. Unlocking c. Extraction d. Ejection

## Slide 5: M17 PRACTICAL EXERCISE
4. What control/indicator on the M17 locks the magazine into the magazine well and releases the magazine?
a. Takedown lever b. Slide catch lever c. Trigger d. Magazine catch
5. What control/indicator on the M17 blocks trigger bar from releasing trigger?
a. Manual safety lever b. Loaded chamber indicator
c. Takedown lever d. Slide catch lever
6. What malfunction on the M17 could cause the cartridge not feeding?
a. Clean ammunition b. Improperly assembled magazine
c. Wrong size grip module c. Safety lever on "Safe"

## Slide 6: M17 PRACTICAL EXERCISE
4. What control/indicator on the M17 locks the magazine into the magazine well and releases the magazine?
a. Takedown lever b. Slide catch lever c. Trigger d. Magazine catch
5. What control/indicator on the M17 blocks trigger bar from releasing trigger?
a. Manual safety lever b. Loaded chamber indicator
c. Takedown lever d. Slide catch lever
6. What malfunction on the M17 could cause the cartridge not feeding?
a. Clean ammunition b. Improperly assembled magazine
c. Wrong size grip module c. Safety lever on "Safe"

## Slide 7: M17 PRACTICAL EXERCISE
4. What control/indicator on the M17 locks the magazine into the magazine well and releases the magazine?
a. Takedown lever b. Slide catch lever c. Trigger d. Magazine catch
5. What control/indicator on the M17 blocks trigger bar from releasing trigger?
a. Manual safety lever b. Loaded chamber indicator
c. Takedown lever d. Slide catch lever
6. What malfunction on the M17 could cause the cartridge not feeding?
a. Clean ammunition b. Improperly assembled magazine
c. Wrong size grip module c. Safety lever on "Safe"

## Slide 8: M17 PRACTICAL EXERCISE
4. What control/indicator on the M17 locks the magazine into the magazine well and releases the magazine?
a. Takedown lever b. Slide catch lever c. Trigger d. Magazine catch
5. What control/indicator on the M17 blocks trigger bar from releasing trigger?
a. Manual safety lever b. Loaded chamber indicator
c. Takedown lever d. Slide catch lever
6. What malfunction on the M17 could cause the cartridge not feeding?
a. Clean ammunition b. Improperly assembled magazine
c. Wrong size grip module c. Safety lever on "Safe"

## Slide 9: M17 PRACTICAL EXERCISE
7. What malfunction could cause the cartridge not to chamber on the M17?
a. Clean ammunition b. Safety lever in the "Safe" position
c. Obstruction in the chamber and bore d. Sufficient lubrication
8. What can cause the slide to not lock fully forward on the M17?
a. Safety lever in "Safe" position b. Clean magazine
c. Improper size grip module d. Dirty ammunition
9. When troubleshooting the M17 pistol does not fire, what corrective action is taken when you find a broken trigger bar?
a. Notify Field/ Maintainer maintenance b. Replace trigger bar
c. Replace magazine d. No action needed

## Slide 10: M17 PRACTICAL EXERCISE
7. What malfunction could cause the cartridge not to chamber on the M17?
a. Clean ammunition b. Safety lever in the "Safe" position
c. Obstruction in the chamber and bore d. Sufficient lubrication
8. What can cause the slide to not lock fully forward on the M17?
a. Safety lever in "Safe" position b. Clean magazine
c. Improper size grip module d. Dirty ammunition
9. When troubleshooting the M17 pistol does not fire, what corrective action is taken when you find a broken trigger bar?
a. Notify Field/ Maintainer maintenance b. Replace trigger bar
c. Replace magazine d. No action needed

## Slide 11: M17 PRACTICAL EXERCISE
7. What malfunction could cause the cartridge not to chamber on the M17?
a. Clean ammunition b. Safety lever in the "Safe" position
c. Obstruction in the chamber and bore d. Sufficient lubrication
8. What can cause the slide to not lock fully forward on the M17?
a. Safety lever in "Safe" position b. Clean magazine
c. Improper size grip module d. Dirty ammunition
9. When troubleshooting the M17 pistol does not fire, what corrective action is taken when you find a broken trigger bar?
a. Notify Field/ Maintainer maintenance b. Replace trigger bar
c. Replace magazine d. No action needed

## Slide 12: M17 PRACTICAL EXERCISE
7. What malfunction could cause the cartridge not to chamber on the M17?
a. Clean ammunition b. Safety lever in the "Safe" position
c. Obstruction in the chamber and bore d. Sufficient lubrication
8. What can cause the slide to not lock fully forward on the M17?
a. Safety lever in "Safe" position b. Clean magazine
c. Improper size grip module d. Dirty ammunition
9. When troubleshooting the M17 pistol does not fire, what corrective action is taken when you find a broken trigger bar?
a. Notify Field/ Maintainer maintenance b. Replace trigger bar
c. Replace magazine d. No action needed

## Slide 13: M17 PRACTICAL EXERCISE
10. What corrective action is needed when the cartridge does not extract because the chamber is dirty on the M17?
a. Notify Field/Maintainer maintenance b. Clean chamber and barrel
c. Issue a different weapon d. No corrective action is needed
11. What malfunction on the M17 could cause a dead trigger?
a. Faulty ammunition b. Weak extractor spring
c. Takedown safety lever improperly positioned d. Operator headspace and timing
12. On the M17, what does the front and rear sights contain?
a. Nothing b. Whiteout
c. CLP d. Tritium

## Slide 14: M17 PRACTICAL EXERCISE
10. What corrective action is needed when the cartridge does not extract because the chamber is dirty on the M17?
a. Notify Field/Maintainer maintenance b. Clean chamber and barrel
c. Issue a different weapon d. No corrective action is needed
11. What malfunction on the M17 could cause a dead trigger?
a. Faulty ammunition b. Weak extractor spring
c. Takedown safety lever improperly positioned d. Operator headspace and timing
12. On the M17, what does the front and rear sights contain?
a. Nothing b. Whiteout
c. CLP d. Tritium

## Slide 15: M17 PRACTICAL EXERCISE
10. What corrective action is needed when the cartridge does not extract because the chamber is dirty on the M17?
a. Notify Field/Maintainer maintenance b. Clean chamber and barrel
c. Issue a different weapon d. No corrective action is needed
11. What malfunction on the M17 could cause a dead trigger?
a. Faulty ammunition b. Weak extractor spring
c. Takedown safety lever improperly positioned d. Operator headspace and timing
12. On the M17, what does the front and rear sights contain?
a. Nothing b. Whiteout
c. CLP d. Tritium

## Slide 16: M17 PRACTICAL EXERCISE
10. What corrective action is needed when the cartridge does not extract because the chamber is dirty on the M17?
a. Notify Field/Maintainer maintenance b. Clean chamber and barrel
c. Issue a different weapon d. No corrective action is needed
11. What malfunction on the M17 could cause a dead trigger?
a. Faulty ammunition b. Weak extractor spring
c. Takedown safety lever improperly positioned d. Operator headspace and timing
12. On the M17, what does the front and rear sights contain?
a. Nothing b. Whiteout
c. CLP d. Tritium

## Slide 17: M17 PRACTICAL EXERCISE
13. The M17 front sights illuminate what color?
a. Green b. Orange c. Red d. Blue
14. What is the first step when disassembling the M17 pistol?
a. Function check b. Unload/clear weapon
c. Insert magazine d. Place the safety lever on "Fire"
15. The operator and/or the armorer can disassemble the M17 magazine?
a. True
b. False

## Slide 18: M17 PRACTICAL EXERCISE
13. The M17 front sights illuminate what color?
a. Green b. Orange c. Red d. Blue
14. What is the first step when disassembling the M17 pistol?
a. Function check b. Unload/clear weapon
c. Insert magazine d. Place the safety lever on "Fire"
15. The operator and/or the armorer can disassemble the M17 magazine?
a. True
b. False

## Slide 19: M17 PRACTICAL EXERCISE
13. The M17 front sights illuminate what color?
a. Green b. Orange c. Red d. Blue
14. What is the first step when disassembling the M17 pistol?
a. Function check b. Unload/clear weapon
c. Insert magazine d. Place the safety lever on "Fire"
15. The operator and/or the armorer can disassemble the M17 magazine?
a. True
b. False

## Slide 20: M17 PRACTICAL EXERCISE
13. The M17 front sights illuminate what color?
a. Green b. Orange c. Red d. Blue
14. What is the first step when disassembling the M17 pistol?
a. Function check b. Unload/clear weapon
c. Insert magazine d. Place the safety lever on "Fire"
15. The operator and/or the armorer can disassemble the M17 magazine?
a. True
b. False

## Slide 21: M17 PRACTICAL EXERCISE
16. What is the first step when inspecting the slide assembly on the M17?
a. Inspect slide/slide rails for burrs/cracks b. Inspect weapon for cleanliness
c. Inspect recoil spring d. Check front and rear sights
17. When inspecting the M17 recoil spring and guide assembly, what must you ensure on the recoil spring?
a. Not broken, bent or damaged b. Free movement of slide catch lever
c. Magazine spring is free from damage d. No cracks on receiver rails
18. When inspecting the M17 receiver/grip module, you must ensure free movement of what component?
a. Magazine spring b. Slide catch lever
c. Recoil spring guide d. Barrel

## Slide 22: M17 PRACTICAL EXERCISE
16. What is the first step when inspecting the slide assembly on the M17?
a. Inspect slide/slide rails for burrs/cracks b. Inspect weapon for cleanliness
c. Inspect recoil spring d. Check front and rear sights
17. When inspecting the M17 recoil spring and guide assembly, what must you ensure on the recoil spring?
a. Not broken, bent or damaged b. Free movement of slide catch lever
c. Magazine spring is free from damage d. No cracks on receiver rails
18. When inspecting the M17 receiver/grip module, you must ensure free movement of what component?
a. Magazine spring b. Slide catch lever
c. Recoil spring guide d. Barrel

## Slide 23: M17 PRACTICAL EXERCISE
16. What is the first step when inspecting the slide assembly on the M17?
a. Inspect slide/slide rails for burrs/cracks b. Inspect weapon for cleanliness
c. Inspect recoil spring d. Check front and rear sights
17. When inspecting the M17 recoil spring and guide assembly, what must you ensure on the recoil spring?
a. Not broken, bent or damaged b. Free movement of slide catch lever
c. Magazine spring is free from damage d. No cracks on receiver rails
18. When inspecting the M17 receiver/grip module, you must ensure free movement of what component?
a. Magazine spring b. Slide catch lever
c. Recoil spring guide d. Barrel

## Slide 24: M17 PRACTICAL EXERCISE
16. What is the first step when inspecting the slide assembly on the M17?
a. Inspect slide/slide rails for burrs/cracks b. Inspect weapon for cleanliness
c. Inspect recoil spring d. Check front and rear sights
17. When inspecting the M17 recoil spring and guide assembly, what must you ensure on the recoil spring?
a. Not broken, bent or damaged b. Free movement of slide catch lever
c. Magazine spring is free from damage d. No cracks on receiver rails
18. When inspecting the M17 receiver/grip module, you must ensure free movement of what component?
a. Magazine spring b. Slide catch lever
c. Recoil spring guide d. Barrel

## Slide 25: M17 PRACTICAL EXERCISE
19. What lubricant is not authorized to use on the M17?
a. CLP b. LAW c. GMD d. LSA
20. On the M17, lightly lubricated means what?
a. Lubricant can be spread with a finger b. Lubricant drips from weapon
c. Cannot see any lubricant film d. Lubricant film barely visible to the eye
21. How should the M17 barrel exterior be lubricated?
a. Lightly lubricated b. Generously lubricated
c. Heavily lubricated d. Lubricant is not authorized

## Slide 26: M17 PRACTICAL EXERCISE
19. What lubricant is not authorized to use on the M17?
a. CLP b. LAW c. GMD d. LSA
20. On the M17, lightly lubricated means what?
a. Lubricant can be spread with a finger b. Lubricant drips from weapon
c. Cannot see any lubricant film d. Lubricant film barely visible to the eye
21. How should the M17 barrel exterior be lubricated?
a. Lightly lubricated b. Generously lubricated
c. Heavily lubricated d. Lubricant is not authorized

## Slide 27: M17 PRACTICAL EXERCISE
19. What lubricant is not authorized to use on the M17?
a. CLP b. LAW c. GMD d. LSA
20. On the M17, lightly lubricated means what?
a. Lubricant can be spread with a finger b. Lubricant drips from weapon
c. Cannot see any lubricant film d. Lubricant film barely visible to the eye
21. How should the M17 barrel exterior be lubricated?
a. Lightly lubricated b. Generously lubricated
c. Heavily lubricated d. Lubricant is not authorized

## Slide 28: M17 PRACTICAL EXERCISE
19. What lubricant is not authorized to use on the M17?
a. CLP b. LAW c. GMD d. LSA
20. On the M17, lightly lubricated means what?
a. Lubricant can be spread with a finger b. Lubricant drips from weapon
c. Cannot see any lubricant film d. Lubricant film barely visible to the eye
21. How should the M17 barrel exterior be lubricated?
a. Lightly lubricated b. Generously lubricated
c. Heavily lubricated d. Lubricant is not authorized

## Slide 29: M17 PRACTICAL EXERCISE
22. What should be lubricated on the M17 receiver/grip module assembly?
a. Recoil spring b. Four receiver rails
c. Spring guide d. Slide bushing
23. What is the last step of the M17 assembly?
a. Install barrel b. Install spring guide assembly
c. Perform safety/function check d. Press down on slide catch lever
24. When performing the safety/function check on the M17, what should happen when pressing the magazine catch?
a. Magazine should lock in place b. Should here an audible click
c. The striker should release d. Magazine must fall free under its own weight

## Slide 30: M17 PRACTICAL EXERCISE
22. What should be lubricated on the M17 receiver/grip module assembly?
a. Recoil spring b. Four receiver rails
c. Spring guide d. Slide bushing
23. What is the last step of the M17 assembly?
a. Install barrel b. Install spring guide assembly
c. Perform safety/function check d. Press down on slide catch lever
24. When performing the safety/function check on the M17, what should happen when pressing the magazine catch?
a. Magazine should lock in place b. Should here an audible click
c. The striker should release d. Magazine must fall free under its own weight

## Slide 31: M17 PRACTICAL EXERCISE
22. What should be lubricated on the M17 receiver/grip module assembly?
a. Recoil spring b. Four receiver rails
c. Spring guide d. Slide bushing
23. What is the last step of the M17 assembly?
a. Install barrel b. Install spring guide assembly
c. Perform safety/function check d. Press down on slide catch lever
24. When performing the safety/function check on the M17, what should happen when pressing the magazine catch?
a. Magazine should lock in place b. Should here an audible click
c. The striker should release d. Magazine must fall free under its own weight

## Slide 32: M17 PRACTICAL EXERCISE
22. What should be lubricated on the M17 receiver/grip module assembly?
a. Recoil spring b. Four receiver rails
c. Spring guide d. Slide bushing
23. What is the last step of the M17 assembly?
a. Install barrel b. Install spring guide assembly
c. Perform safety/function check d. Press down on slide catch lever
24. When performing the safety/function check on the M17, what should happen when pressing the magazine catch?
a. Magazine should lock in place b. Should here an audible click
c. The striker should release d. Magazine must fall free under its own weight

## Slide 33: M17 PRACTICAL EXERCISE
25. Which one of these can the unit armorer perform on the M17?
a. Grip module replacement b. Disassemble the trigger mechanism
c. Reverse magazine catch d. None of these
26. When sizing the grip module on the M17 to the shooter, how should the shooters trigger finger lay on the trigger?
a. Shooter should alter grip to reach trigger b. Finger should lay comfortably across trigger
c. Entire finger should be across trigger d. It doesn't matter how finger is positioned
27. How many grip assemblies are authorized for use on the M17?
a. 1 b. 2 c. 3 d. 4

## Slide 34: M17 PRACTICAL EXERCISE
25. Which one of these can the unit armorer perform on the M17?
a. Grip module replacement b. Disassemble the trigger mechanism
c. Reverse magazine catch d. None of these
26. When sizing the grip module on the M17 to the shooter, how should the shooters trigger finger lay on the trigger?
a. Shooter should alter grip to reach trigger b. Finger should lay comfortably across trigger
c. Entire finger should be across trigger d. It doesn't matter how finger is positioned
27. How many grip assemblies are authorized for use on the M17?
a. 1 b. 2 c. 3 d. 4

## Slide 35: M17 PRACTICAL EXERCISE
25. Which one of these can the unit armorer perform on the M17?
a. Grip module replacement b. Disassemble the trigger mechanism
c. Reverse magazine catch d. None of these
26. When sizing the grip module on the M17 to the shooter, how should the shooters trigger finger lay on the trigger?
a. Shooter should alter grip to reach trigger b. Finger should lay comfortably across trigger
c. Entire finger should be across trigger d. It doesn't matter how finger is positioned
27. How many grip assemblies are authorized for use on the M17?
a. 1 b. 2 c. 3 d. 4

## Slide 36: M17 PRACTICAL EXERCISE
25. Which one of these can the unit armorer perform on the M17?
a. Grip module replacement b. Disassemble the trigger mechanism
c. Reverse magazine catch d. None of these
26. When sizing the grip module on the M17 to the shooter, how should the shooters trigger finger lay on the trigger?
a. Shooter should alter grip to reach trigger b. Finger should lay comfortably across trigger
c. Entire finger should be across trigger d. It doesn't matter how finger is positioned
27. How many grip assemblies are authorized for use on the M17?
a. 1 b. 2 c. 3 d. 4

## Slide 37: M17 PRACTICAL EXERCISE
28. What is the NSN for the small arms swab for the M17?
a. 1005-00-716-2132 b. 1005-00-494-6602
c. 1005-00-556-4102 d. 1005-00-288-3565
29. What is the term used to describe corrosion cracking and corrosion fatigue on the M17?
a. Stress b. Pitting c. Erosion d. Fretting
30. What control/indicator on the M17 provides a visual and physical indicator when a cartridge is loaded in the chamber?
a. Takedown lever b. Slide catch lever
c. Magazine catch d. Loaded chamber indicator

## Slide 38: M17 PRACTICAL EXERCISE
28. What is the NSN for the small arms swab for the M17?
a. 1005-00-716-2132 b. 1005-00-494-6602
c. 1005-00-556-4102 d. 1005-00-288-3565
29. What is the term used to describe corrosion cracking and corrosion fatigue on the M17?
a. Stress b. Pitting c. Erosion d. Fretting
30. What control/indicator on the M17 provides a visual and physical indicator when a cartridge is loaded in the chamber?
a. Takedown lever b. Slide catch lever
c. Magazine catch d. Loaded chamber indicator

## Slide 39: M17 PRACTICAL EXERCISE
28. What is the NSN for the small arms swab for the M17?
a. 1005-00-716-2132 b. 1005-00-494-6602
c. 1005-00-556-4102 d. 1005-00-288-3565
29. What is the term used to describe corrosion cracking and corrosion fatigue on the M17?
a. Stress b. Pitting c. Erosion d. Fretting
30. What control/indicator on the M17 provides a visual and physical indicator when a cartridge is loaded in the chamber?
a. Takedown lever b. Slide catch lever
c. Magazine catch d. Loaded chamber indicator

## Slide 40: M17 PRACTICAL EXERCISE
28. What is the NSN for the small arms swab for the M17?
a. 1005-00-716-2132 b. 1005-00-494-6602
c. 1005-00-556-4102 d. 1005-00-288-3565
29. What is the term used to describe corrosion cracking and corrosion fatigue on the M17?
a. Stress b. Pitting c. Erosion d. Fretting
30. What control/indicator on the M17 provides a visual and physical indicator when a cartridge is loaded in the chamber?
a. Takedown lever b. Slide catch lever
c. Magazine catch d. Loaded chamber indicator