## Slide 1
M240 SERIES MACHINE GUN WRITTEN PE
The M240 MG is belt fed from the ___________?
Right side b. Left side c. Only magazine fed d. Bottom
The M-240 Series Machine Gun employs ___________ operation?
Recoil b. Gas c. Blowback d. Manually
The M-240C Machine Gun is belt fed from the ___________ side?
Right hand
Is capable of both right and left hand feed
It is manually fed
Left hand
IAW DA PAM 750-8, the completed Quarterly services are maintained for the M240 series MG?
180 days
90 days
Until the next service is completed
d. 1 year

## Slide 2
M240 SERIES MACHINE GUN WRITTEN PE
The M240 MG is belt fed from the ___________?
Right side b. Left side c. Only magazine fed d. Bottom
The M-240 Series Machine Gun employs ___________ operation?
Recoil b. Gas c. Blowback d. Manually
The M-240C Machine Gun is belt fed from the ___________ side?
Right hand
Is capable of both right and left hand feed
It is manually fed
Left hand
IAW DA PAM 750-8, the completed Quarterly services are maintained for the M240 series MG?
180 days
90 days
Until the next service is completed
d. 1 year

## Slide 3
M240 SERIES MACHINE GUN WRITTEN PE
The M240 MG is belt fed from the ___________?
Right side b. Left side c. Only magazine fed d. Bottom
The M-240 Series Machine Gun employs ___________ operation?
Recoil b. Gas c. Blowback d. Manually
The M-240C Machine Gun is belt fed from the ___________ side?
Right hand
Is capable of both right and left hand feed
It is manually fed
Left hand
IAW DA PAM 750-8, the completed Quarterly services are maintained for the M240 series MG?
180 days
90 days
Until the next service is completed
d. 1 year

## Slide 4
M240 SERIES MACHINE GUN WRITTEN PE
The M240 MG is belt fed from the ___________?
Right side b. Left side c. Only magazine fed d. Bottom
The M-240 Series Machine Gun employs ___________ operation?
Recoil b. Gas c. Blowback d. Manually
The M-240C Machine Gun is belt fed from the ___________ side?
Right hand
Is capable of both right and left hand feed
It is manually fed
Left hand
IAW DA PAM 750-8, the completed Quarterly services are maintained for the M240 series MG?
180 days
90 days
Until the next service is completed
d. 1 year

## Slide 5
M240 SERIES MACHINE GUN WRITTEN PE
The M240 MG is belt fed from the ___________?
Right side b. Left side c. Only magazine fed d. Bottom
The M-240 Series Machine Gun employs ___________ operation?
Recoil b. Gas c. Blowback d. Manually
The M-240C Machine Gun is belt fed from the ___________ side?
Right hand
Is capable of both right and left hand feed
It is manually fed
Left hand
IAW DA PAM 750-8, the completed Quarterly services are maintained for the M240 series MG?
180 days
90 days
Until the next service is completed
d. 1 year

## Slide 6
M240 SERIES MACHINE GUN WRITTEN PE
5. The setting for normal rate of fire on the M240 is in what position?
One b. Two c. Three d. All the above
Preventive maintenance checks and services on the M240 series MG are performed how often?
Weekly b. Monthly c. Quarterly d. Daily
7. When installing barrel assembly into receiver on the M240 series MG, less than two or more than seven clicks
Indicates what?
a. Defective parts
b. That the barrel assembly is serviceable
c. That the receiver is serviceable
d. That the barrel release is serviceable
Which parts should not be lubricated prior to firing the M240 series MG?
a. Trigger assembly
b. Bolt
c. Gas piston
d. Back plate

## Slide 7
M240 SERIES MACHINE GUN WRITTEN PE
5. The setting for normal rate of fire on the M240 is in what position?
One b. Two c. Three d. All the above
Preventive maintenance checks and services on the M240 series MG are performed how often?
Weekly b. Monthly c. Quarterly d. Daily
7. When installing barrel assembly into receiver on the M240 series MG, less than two or more than seven clicks
Indicates what?
a. Defective parts
b. That the barrel assembly is serviceable
c. That the receiver is serviceable
d. That the barrel release is serviceable
Which parts should not be lubricated prior to firing the M240 series MG?
a. Trigger assembly
b. Bolt
c. Gas piston
d. Back plate

## Slide 8
M240 SERIES MACHINE GUN WRITTEN PE
5. The setting for normal rate of fire on the M240 is in what position?
One b. Two c. Three d. All the above
Preventive maintenance checks and services on the M240 series MG are performed how often?
Weekly b. Monthly c. Quarterly d. Daily
7. When installing barrel assembly into receiver on the M240 series MG, less than two or more than seven clicks
Indicates what?
a. Defective parts
b. That the barrel assembly is serviceable
c. That the receiver is serviceable
d. That the barrel release is serviceable
Which parts should not be lubricated prior to firing the M240 series MG?
a. Trigger assembly
b. Bolt
c. Gas piston
d. Back plate

## Slide 9
M240 SERIES MACHINE GUN WRITTEN PE
5. The setting for normal rate of fire on the M240 is in what position?
One b. Two c. Three d. All the above
Preventive maintenance checks and services on the M240 series MG are performed how often?
Weekly b. Monthly c. Quarterly d. Daily
7. When installing barrel assembly into receiver on the M240 series MG, less than two or more than seven clicks
Indicates what?
a. Defective parts
b. That the barrel assembly is serviceable
c. That the receiver is serviceable
d. That the barrel release is serviceable
Which parts should not be lubricated prior to firing the M240 series MG?
a. Trigger assembly
b. Bolt
c. Gas piston
d. Back plate

## Slide 10
M240 SERIES MACHINE GUN WRITTEN PE
5. The setting for normal rate of fire on the M240 is in what position?
One b. Two c. Three d. All the above
Preventive maintenance checks and services on the M240 series MG are performed how often?
Weekly b. Monthly c. Quarterly d. Daily
7. When installing barrel assembly into receiver on the M240 series MG, less than two or more than seven clicks
Indicates what?
a. Defective parts
b. That the barrel assembly is serviceable
c. That the receiver is serviceable
d. That the barrel release is serviceable
Which parts should not be lubricated prior to firing the M240 series MG?
a. Trigger assembly
b. Bolt
c. Gas piston
d. Back plate

## Slide 11
M240 SERIES MACHINE GUN WRITTEN PE
The M240 gas regulator plug is designed with how many inlet settings to maintain the rate of fire?
a. Three b. Two c. Four d. One
Of the following items, which one is NMC on the M240 series MG?
a. Less than 1/3 exterior surface b. Bipod leg damaged
c. Frayed sling d. Missing barrel patches
IAW DA PAM 750-8, a completed/closed work request (DA 5990-E) on the M240 series MG is maintained for how long?
a. 1 year b. 180 days c. 2 years d. 90 days
How many current models of the M240 series machine gun are there?
a. (5)
b. (7)
c. (9)
d. (8)

## Slide 12
M240 SERIES MACHINE GUN WRITTEN PE
The M240 gas regulator plug is designed with how many inlet settings to maintain the rate of fire?
a. Three b. Two c. Four d. One
Of the following items, which one is NMC on the M240 series MG?
a. Less than 1/3 exterior surface b. Bipod leg damaged
c. Frayed sling d. Missing barrel patches
IAW DA PAM 750-8, a completed/closed work request (DA 5990-E) on the M240 series MG is maintained for how long?
a. 1 year b. 180 days c. 2 years d. 90 days
How many current models of the M240 series machine gun are there?
a. (5)
b. (7)
c. (9)
d. (8)

## Slide 13
M240 SERIES MACHINE GUN WRITTEN PE
The M240 gas regulator plug is designed with how many inlet settings to maintain the rate of fire?
a. Three b. Two c. Four d. One
Of the following items, which one is NMC on the M240 series MG?
a. Less than 1/3 exterior surface b. Bipod leg damaged
c. Frayed sling d. Missing barrel patches
IAW DA PAM 750-8, a completed/closed work request (DA 5990-E) on the M240 series MG is maintained for how long?
a. 1 year b. 180 days c. 2 years d. 90 days
How many current models of the M240 series machine gun are there?
a. (5)
b. (7)
c. (9)
d. (8)

## Slide 14
M240 SERIES MACHINE GUN WRITTEN PE
The M240 gas regulator plug is designed with how many inlet settings to maintain the rate of fire?
a. Three b. Two c. Four d. One
Of the following items, which one is NMC on the M240 series MG?
a. Less than 1/3 exterior surface b. Bipod leg damaged
c. Frayed sling d. Missing barrel patches
IAW DA PAM 750-8, a completed/closed work request (DA 5990-E) on the M240 series MG is maintained for how long?
a. 1 year b. 180 days c. 2 years d. 90 days
How many current models of the M240 series machine gun are there?
a. (5)
b. (7)
c. (9)
d. (8)

## Slide 15
M240 SERIES MACHINE GUN WRITTEN PE
The M240 gas regulator plug is designed with how many inlet settings to maintain the rate of fire?
a. Three b. Two c. Four d. One
Of the following items, which one is NMC on the M240 series MG?
a. Less than 1/3 exterior surface b. Bipod leg damaged
c. Frayed sling d. Missing barrel patches
IAW DA PAM 750-8, a completed/closed work request (DA 5990-E) on the M240 series MG is maintained for how long?
a. 1 year b. 180 days c. 2 years d. 90 days
How many current models of the M240 series machine gun are there?
a. (5)
b. (7)
c. (9)
d. (8)

## Slide 16
M240 SERIES MACHINE GUN WRITTEN PE
Sluggish operation on the M240 series MG could be caused by?
a. Loose bipod b. Receiver dirty c. Broken firing pin d. Chipped extractor
14. An M240 series MG damaged gas plug could cause a failure to?
a. Extract b. Cock c. Chamber d. Eject
A runaway M240 series MG could be caused by?
a. Damaged recoil spring b. Missing ejector c. Worn sear d. Damaged buffer
The M-240 Series Machine Gun fires from the _______ bolt position?
a. Closed b. Centered c. Open d. None of the above

## Slide 17
M240 SERIES MACHINE GUN WRITTEN PE
Sluggish operation on the M240 series MG could be caused by?
a. Loose bipod b. Receiver dirty c. Broken firing pin d. Chipped extractor
14. An M240 series MG damaged gas plug could cause a failure to?
a. Extract b. Cock c. Chamber d. Eject
A runaway M240 series MG could be caused by?
a. Damaged recoil spring b. Missing ejector c. Worn sear d. Damaged buffer
The M-240 Series Machine Gun fires from the _______ bolt position?
a. Closed b. Centered c. Open d. None of the above

## Slide 18
M240 SERIES MACHINE GUN WRITTEN PE
Sluggish operation on the M240 series MG could be caused by?
a. Loose bipod b. Receiver dirty c. Broken firing pin d. Chipped extractor
14. An M240 series MG damaged gas plug could cause a failure to?
a. Extract b. Cock c. Chamber d. Eject
A runaway M240 series MG could be caused by?
a. Damaged recoil spring b. Missing ejector c. Worn sear d. Damaged buffer
The M-240 Series Machine Gun fires from the _______ bolt position?
a. Closed b. Centered c. Open d. None of the above

## Slide 19
M240 SERIES MACHINE GUN WRITTEN PE
Sluggish operation on the M240 series MG could be caused by?
a. Loose bipod b. Receiver dirty c. Broken firing pin d. Chipped extractor
14. An M240 series MG damaged gas plug could cause a failure to?
a. Extract b. Cock c. Chamber d. Eject
A runaway M240 series MG could be caused by?
a. Damaged recoil spring b. Missing ejector c. Worn sear d. Damaged buffer
The M-240 Series Machine Gun fires from the _______ bolt position?
a. Closed b. Centered c. Open d. None of the above

## Slide 20
M240 SERIES MACHINE GUN WRITTEN PE
Sluggish operation on the M240 series MG could be caused by?
a. Loose bipod b. Receiver dirty c. Broken firing pin d. Chipped extractor
14. An M240 series MG damaged gas plug could cause a failure to?
a. Extract b. Cock c. Chamber d. Eject
A runaway M240 series MG could be caused by?
a. Damaged recoil spring b. Missing ejector c. Worn sear d. Damaged buffer
The M-240 Series Machine Gun fires from the _______ bolt position?
a. Closed b. Centered c. Open d. None of the above

## Slide 21
M240 SERIES MACHINE GUN WRITTEN PE
During what step in the cycle of operation for the M240 series MG does the ejector compress into the face of the bolt?
a. Locking b. Ejecting c. Feeding d. Chambering
Using the SMR code, which parts on the M249 series MG are replaceable by the armorer?
a. Buffer b. Trigger springer c. Extractor assembly d. None of the above
What is the source of power to move the M240 series MG bolt and operating rod assembly forward during chambering?
a. Gas pressure b. Recoil of the bolt c. Driving spring rod d. All of the bolt
What component holds the M240 series MG bolt and operating rod assembly to the rear in a cocked position?
a. Sear b. Buffer c. Gas pressure d. Trigger pin

## Slide 22
M240 SERIES MACHINE GUN WRITTEN PE
During what step in the cycle of operation for the M240 series MG does the ejector compress into the face of the bolt?
a. Locking b. Ejecting c. Feeding d. Chambering
Using the SMR code, which parts on the M249 series MG are replaceable by the armorer?
a. Buffer b. Trigger springer c. Extractor assembly d. None of the above
What is the source of power to move the M240 series MG bolt and operating rod assembly forward during chambering?
a. Gas pressure b. Recoil of the bolt c. Driving spring rod d. All of the bolt
What component holds the M240 series MG bolt and operating rod assembly to the rear in a cocked position?
a. Sear b. Buffer c. Gas pressure d. Trigger pin

## Slide 23
M240 SERIES MACHINE GUN WRITTEN PE
During what step in the cycle of operation for the M240 series MG does the ejector compress into the face of the bolt?
a. Locking b. Ejecting c. Feeding d. Chambering
Using the SMR code, which parts on the M249 series MG are replaceable by the armorer?
a. Buffer b. Trigger springer c. Extractor assembly d. None of the above
What is the source of power to move the M240 series MG bolt and operating rod assembly forward during chambering?
a. Gas pressure b. Recoil of the bolt c. Driving spring rod d. All of the bolt
What component holds the M240 series MG bolt and operating rod assembly to the rear in a cocked position?
a. Sear b. Buffer c. Gas pressure d. Trigger pin

## Slide 24
M240 SERIES MACHINE GUN WRITTEN PE
During what step in the cycle of operation for the M240 series MG does the ejector compress into the face of the bolt?
a. Locking b. Ejecting c. Feeding d. Chambering
Using the SMR code, which parts on the M249 series MG are replaceable by the armorer?
a. Buffer b. Trigger springer c. Extractor assembly d. None of the above
What is the source of power to move the M240 series MG bolt and operating rod assembly forward during chambering?
a. Gas pressure b. Recoil of the bolt c. Driving spring rod d. All of the bolt
What component holds the M240 series MG bolt and operating rod assembly to the rear in a cocked position?
a. Sear b. Buffer c. Gas pressure d. Trigger pin

## Slide 25
M240 SERIES MACHINE GUN WRITTEN PE
During what step in the cycle of operation for the M240 series MG does the ejector compress into the face of the bolt?
a. Locking b. Ejecting c. Feeding d. Chambering
Using the SMR code, which parts on the M249 series MG are replaceable by the armorer?
a. Buffer b. Trigger springer c. Extractor assembly d. None of the above
What is the source of power to move the M240 series MG bolt and operating rod assembly forward during chambering?
a. Gas pressure b. Recoil of the bolt c. Driving spring rod d. All of the bolt
What component holds the M240 series MG bolt and operating rod assembly to the rear in a cocked position?
a. Sear b. Buffer c. Gas pressure d. Trigger pin

## Slide 26
M240 SERIES MACHINE GUN WRITTEN PE
Which of the following on the M240 series MG would cause a failure to feed?
a. Defective extractor b. Defective barrel release
c. Damaged feed tray d. Defective ejector spring
What malfunction causes a failure to fire on the M240 series MG?
a. Driving spring rod assembly damaged b. Loose rivets causing drag on bolt/operating rod assembly
c. Receiver dirty and/or lack of lubricant d. All of the above
Which of the following would NOT cause a failure to cock on the M240 series MG?
a. Broken trigger spring b. Worn firing pin
c. Broken sear spring d. Worn sear notch on the bolt and operating rod
Which of the following on the M240 series MG would cause a failure to eject?
a. Damaged ejector spring b. Extractor frozen into the face of the bolt
c. Carbon accumulation on the firing pin aperture d. None of the above
Ruptured cartridges in the M240 series MG could be caused by?
a. Bent feed tray b. Defective trigger c. Improper headspace d. None of the above

## Slide 27
M240 SERIES MACHINE GUN WRITTEN PE
Which of the following on the M240 series MG would cause a failure to feed?
a. Defective extractor b. Defective barrel release
c. Damaged feed tray d. Defective ejector spring
What malfunction causes a failure to fire on the M240 series MG?
a. Driving spring rod assembly damaged b. Loose rivets causing drag on bolt/operating rod assembly
c. Receiver dirty and/or lack of lubricant d. All of the above
Which of the following would NOT cause a failure to cock on the M240 series MG?
a. Broken trigger spring b. Worn firing pin
c. Broken sear spring d. Worn sear notch on the bolt and operating rod
Which of the following on the M240 series MG would cause a failure to eject?
a. Damaged ejector spring b. Extractor frozen into the face of the bolt
c. Carbon accumulation on the firing pin aperture d. None of the above
Ruptured cartridges in the M240 series MG could be caused by?
a. Bent feed tray b. Defective trigger c. Improper headspace d. None of the above

## Slide 28
M240 SERIES MACHINE GUN WRITTEN PE
Which of the following on the M240 series MG would cause a failure to feed?
a. Defective extractor b. Defective barrel release
c. Damaged feed tray d. Defective ejector spring
What malfunction causes a failure to fire on the M240 series MG?
a. Driving spring rod assembly damaged b. Loose rivets causing drag on bolt/operating rod assembly
c. Receiver dirty and/or lack of lubricant d. All of the above
Which of the following would NOT cause a failure to cock on the M240 series MG?
a. Broken trigger spring b. Worn firing pin
c. Broken sear spring d. Worn sear notch on the bolt and operating rod
Which of the following on the M240 series MG would cause a failure to eject?
a. Damaged ejector spring b. Extractor frozen into the face of the bolt
c. Carbon accumulation on the firing pin aperture d. None of the above
Ruptured cartridges in the M240 series MG could be caused by?
a. Bent feed tray b. Defective trigger c. Improper headspace d. None of the above

## Slide 29
M240 SERIES MACHINE GUN WRITTEN PE
Which of the following on the M240 series MG would cause a failure to feed?
a. Defective extractor b. Defective barrel release
c. Damaged feed tray d. Defective ejector spring
What malfunction causes a failure to fire on the M240 series MG?
a. Driving spring rod assembly damaged b. Loose rivets causing drag on bolt/operating rod assembly
c. Receiver dirty and/or lack of lubricant d. All of the above
Which of the following would NOT cause a failure to cock on the M240 series MG?
a. Broken trigger spring b. Worn firing pin
c. Broken sear spring d. Worn sear notch on the bolt and operating rod
Which of the following on the M240 series MG would cause a failure to eject?
a. Damaged ejector spring b. Extractor frozen into the face of the bolt
c. Carbon accumulation on the firing pin aperture d. None of the above
Ruptured cartridges in the M240 series MG could be caused by?
a. Bent feed tray b. Defective trigger c. Improper headspace d. None of the above

## Slide 30
M240 SERIES MACHINE GUN WRITTEN PE
Which of the following on the M240 series MG would cause a failure to feed?
a. Defective extractor b. Defective barrel release
c. Damaged feed tray d. Defective ejector spring
What malfunction causes a failure to fire on the M240 series MG?
a. Driving spring rod assembly damaged b. Loose rivets causing drag on bolt/operating rod assembly
c. Receiver dirty and/or lack of lubricant d. All of the above
Which of the following would NOT cause a failure to cock on the M240 series MG?
a. Broken trigger spring b. Worn firing pin
c. Broken sear spring d. Worn sear notch on the bolt and operating rod
Which of the following on the M240 series MG would cause a failure to eject?
a. Damaged ejector spring b. Extractor frozen into the face of the bolt
c. Carbon accumulation on the firing pin aperture d. None of the above
Ruptured cartridges in the M240 series MG could be caused by?
a. Bent feed tray b. Defective trigger c. Improper headspace d. None of the above

## Slide 31
M240 SERIES MACHINE GUN WRITTEN PE
Which of the following on the M240 series MG would cause a failure to feed?
a. Defective extractor b. Defective barrel release
c. Damaged feed tray d. Defective ejector spring
What malfunction causes a failure to fire on the M240 series MG?
a. Driving spring rod assembly damaged b. Loose rivets causing drag on bolt/operating rod assembly
c. Receiver dirty and/or lack of lubricant d. All of the above
Which of the following would NOT cause a failure to cock on the M240 series MG?
a. Broken trigger spring b. Worn firing pin
c. Broken sear spring d. Worn sear notch on the bolt and operating rod
Which of the following on the M240 series MG would cause a failure to eject?
a. Damaged ejector spring b. Extractor frozen into the face of the bolt
c. Carbon accumulation on the firing pin aperture d. None of the above
Ruptured cartridges in the M240 series MG could be caused by?
a. Bent feed tray b. Defective trigger c. Improper headspace d. None of the above

## Slide 32
M240 SERIES MACHINE GUN WRITTEN PE
26. What item on the M240 series MG serves as a support for all major components?
a. Receiver Assembly b. Trigger c. Buttstock d. Cover Assembly
27. What is the description of the buffer assembly for the M240 series MG?
a. Absorbs recoil for bolt and operating rod assembly at the end of recoil movement.
b. Controls the firing of the machine gun.
c. Serves as a guide for positioning cartridges to assist in chambering.
d. Provides energy for returning bolt and operating rod assembly to firing position.
28. What component in the M240 series MG serves as a guide for positioning cartridges to assist in chambering?
a. Feed Tray b. Sear spring c. Receiver Assembly d. Headspace
29. What is the first step of functioning for the M240 series MG?
a. Chambering
b. Feeding
c. Cocking
d. Locking

## Slide 33
M240 SERIES MACHINE GUN WRITTEN PE
26. What item on the M240 series MG serves as a support for all major components?
a. Receiver Assembly b. Trigger c. Buttstock d. Cover Assembly
27. What is the description of the buffer assembly for the M240 series MG?
a. Absorbs recoil for bolt and operating rod assembly at the end of recoil movement.
b. Controls the firing of the machine gun.
c. Serves as a guide for positioning cartridges to assist in chambering.
d. Provides energy for returning bolt and operating rod assembly to firing position.
28. What component in the M240 series MG serves as a guide for positioning cartridges to assist in chambering?
a. Feed Tray b. Sear spring c. Receiver Assembly d. Headspace
29. What is the first step of functioning for the M240 series MG?
a. Chambering
b. Feeding
c. Cocking
d. Locking

## Slide 34
M240 SERIES MACHINE GUN WRITTEN PE
26. What item on the M240 series MG serves as a support for all major components?
a. Receiver Assembly b. Trigger c. Buttstock d. Cover Assembly
27. What is the description of the buffer assembly for the M240 series MG?
a. Absorbs recoil for bolt and operating rod assembly at the end of recoil movement.
b. Controls the firing of the machine gun.
c. Serves as a guide for positioning cartridges to assist in chambering.
d. Provides energy for returning bolt and operating rod assembly to firing position.
28. What component in the M240 series MG serves as a guide for positioning cartridges to assist in chambering?
a. Feed Tray b. Sear spring c. Receiver Assembly d. Headspace
29. What is the first step of functioning for the M240 series MG?
a. Chambering
b. Feeding
c. Cocking
d. Locking

## Slide 35
M240 SERIES MACHINE GUN WRITTEN PE
26. What item on the M240 series MG serves as a support for all major components?
a. Receiver Assembly b. Trigger c. Buttstock d. Cover Assembly
27. What is the description of the buffer assembly for the M240 series MG?
a. Absorbs recoil for bolt and operating rod assembly at the end of recoil movement.
b. Controls the firing of the machine gun.
c. Serves as a guide for positioning cartridges to assist in chambering.
d. Provides energy for returning bolt and operating rod assembly to firing position.
28. What component in the M240 series MG serves as a guide for positioning cartridges to assist in chambering?
a. Feed Tray b. Sear spring c. Receiver Assembly d. Headspace
29. What is the first step of functioning for the M240 series MG?
a. Chambering
b. Feeding
c. Cocking
d. Locking

## Slide 36
M240 SERIES MACHINE GUN WRITTEN PE
26. What item on the M240 series MG serves as a support for all major components?
a. Receiver Assembly b. Trigger c. Buttstock d. Cover Assembly
27. What is the description of the buffer assembly for the M240 series MG?
a. Absorbs recoil for bolt and operating rod assembly at the end of recoil movement.
b. Controls the firing of the machine gun.
c. Serves as a guide for positioning cartridges to assist in chambering.
d. Provides energy for returning bolt and operating rod assembly to firing position.
28. What component in the M240 series MG serves as a guide for positioning cartridges to assist in chambering?
a. Feed Tray b. Sear spring c. Receiver Assembly d. Headspace
29. What is the first step of functioning for the M240 series MG?
a. Chambering
b. Feeding
c. Cocking
d. Locking

## Slide 37
M240 SERIES MACHINE GUN WRITTEN PE
30. What cycle of function on the M240 series MG can only take place after locking of the bolt?
a. Unlocking
b. Feeding
c. Firing
d. Extracting

## Slide 38
M240 SERIES MACHINE GUN WRITTEN PE
30. What cycle of function on the M240 series MG can only take place after locking of the bolt?
a. Unlocking
b. Feeding
c. Firing
d. Extracting