## Slide 1
M249 WRITTEN PE
1. How is the M249 operated?
a. Blowback b. Recoil c. Gas d. Manually
2. Using the SMR code, the armorer can replace which part on the M249?
a. Safety b. Grip assembly c. Sear spring d. None of these
3. The M249 machine gun is fired from what bolt position?
a. Open b. Closed c. Centered d. None of the above
4. If the safety on the M249 fails to slide properly after cleaning, what corrective action would you take?
a. Replace safety b. Send to depot c. Send to field maintenance d. None of the above
5. A damaged feed tray could cause a failure to?
a. Feed b. Extract c. Fire d. None of the above

## Slide 2
M249 WRITTEN PE
1. How is the M249 operated?
a. Blowback b. Recoil c. Gas d. Manually
2. Using the SMR code, the armorer can replace which part on the M249?
a. Safety b. Grip assembly c. Sear spring d. None of these
3. The M249 machine gun is fired from what bolt position?
a. Open b. Closed c. Centered d. None of the above
4. If the safety on the M249 fails to slide properly after cleaning, what corrective action would you take?
a. Replace safety b. Send to depot c. Send to field maintenance d. None of the above
5. A damaged feed tray could cause a failure to?
a. Feed b. Extract c. Fire d. None of the above

## Slide 3
M249 WRITTEN PE
1. How is the M249 operated?
a. Blowback b. Recoil c. Gas d. Manually
2. Using the SMR code, the armorer can replace which part on the M249?
a. Safety b. Grip assembly c. Sear spring d. None of these
3. The M249 machine gun is fired from what bolt position?
a. Open b. Closed c. Centered d. None of the above
4. If the safety on the M249 fails to slide properly after cleaning, what corrective action would you take?
a. Replace safety b. Send to depot c. Send to field maintenance d. None of the above
5. A damaged feed tray could cause a failure to?
a. Feed b. Extract c. Fire d. None of the above

## Slide 4
M249 WRITTEN PE
1. How is the M249 operated?
a. Blowback b. Recoil c. Gas d. Manually
2. Using the SMR code, the armorer can replace which part on the M249?
a. Safety b. Grip assembly c. Sear spring d. None of these
3. The M249 machine gun is fired from what bolt position?
a. Open b. Closed c. Centered d. None of the above
4. If the safety on the M249 fails to slide properly after cleaning, what corrective action would you take?
a. Replace safety b. Send to depot c. Send to field maintenance d. None of the above
5. A damaged feed tray could cause a failure to?
a. Feed b. Extract c. Fire d. None of the above

## Slide 5
M249 WRITTEN PE
1. How is the M249 operated?
a. Blowback b. Recoil c. Gas d. Manually
2. Using the SMR code, the armorer can replace which part on the M249?
a. Safety b. Grip assembly c. Sear spring d. None of these
3. The M249 machine gun is fired from what bolt position?
a. Open b. Closed c. Centered d. None of the above
4. If the safety on the M249 fails to slide properly after cleaning, what corrective action would you take?
a. Replace safety b. Send to depot c. Send to field maintenance d. None of the above
5. A damaged feed tray could cause a failure to?
a. Feed b. Extract c. Fire d. None of the above

## Slide 6
M249 WRITTEN PE
1. How is the M249 operated?
a. Blowback b. Recoil c. Gas d. Manually
2. Using the SMR code, the armorer can replace which part on the M249?
a. Safety b. Grip assembly c. Sear spring d. None of these
3. The M249 machine gun is fired from what bolt position?
a. Open b. Closed c. Centered d. None of the above
4. If the safety on the M249 fails to slide properly after cleaning, what corrective action would you take?
a. Replace safety b. Send to depot c. Send to field maintenance d. None of the above
5. A damaged feed tray could cause a failure to?
a. Feed b. Extract c. Fire d. None of the above

## Slide 7
M249 WRITTEN PE
What is the corrective action for a plugged gas regulator (mono-block) on the M249?
a. (O) b. (H) c. (F) d. (D)
On the M249, a failure to extract could be caused by?
a. Ejector worn b. Insufficient gas pressure c. Loose tower d. Firing pin damaged
8. A defective M249 sear could cause a failure to?
a. Lock b. Feed c. Cock d. Unlock
The M249 machine gun
a. Is a semi-automatic weapon
b. Is belt or magazine fed
c. Fires from the close bolt position
d. Is recoil operated
The M249 tripping lever is attached to the?
a. Sear b. Bolt c. Safety d. None of the above

## Slide 8
M249 WRITTEN PE
What is the corrective action for a plugged gas regulator (mono-block) on the M249?
a. (O) b. (H) c. (F) d. (D)
On the M249, a failure to extract could be caused by?
a. Ejector worn b. Insufficient gas pressure c. Loose tower d. Firing pin damaged
8. A defective M249 sear could cause a failure to?
a. Lock b. Feed c. Cock d. Unlock
The M249 machine gun
a. Is a semi-automatic weapon
b. Is belt or magazine fed
c. Fires from the close bolt position
d. Is recoil operated
The M249 tripping lever is attached to the?
a. Sear b. Bolt c. Safety d. None of the above

## Slide 9
M249 WRITTEN PE
What is the corrective action for a plugged gas regulator (mono-block) on the M249?
a. (O) b. (H) c. (F) d. (D)
On the M249, a failure to extract could be caused by?
a. Ejector worn b. Insufficient gas pressure c. Loose tower d. Firing pin damaged
8. A defective M249 sear could cause a failure to?
a. Lock b. Feed c. Cock d. Unlock
The M249 machine gun
a. Is a semi-automatic weapon
b. Is belt or magazine fed
c. Fires from the close bolt position
d. Is recoil operated
The M249 tripping lever is attached to the?
a. Sear b. Bolt c. Safety d. None of the above

## Slide 10
M249 WRITTEN PE
What is the corrective action for a plugged gas regulator (mono-block) on the M249?
a. (O) b. (H) c. (F) d. (D)
On the M249, a failure to extract could be caused by?
a. Ejector worn b. Insufficient gas pressure c. Loose tower d. Firing pin damaged
8. A defective M249 sear could cause a failure to?
a. Lock b. Feed c. Cock d. Unlock
The M249 machine gun
a. Is a semi-automatic weapon
b. Is belt or magazine fed
c. Fires from the close bolt position
d. Is recoil operated
The M249 tripping lever is attached to the?
a. Sear b. Bolt c. Safety d. None of the above

## Slide 11
M249 WRITTEN PE
What is the corrective action for a plugged gas regulator (mono-block) on the M249?
a. (O) b. (H) c. (F) d. (D)
On the M249, a failure to extract could be caused by?
a. Ejector worn b. Insufficient gas pressure c. Loose tower d. Firing pin damaged
8. A defective M249 sear could cause a failure to?
a. Lock b. Feed c. Cock d. Unlock
The M249 machine gun
a. Is a semi-automatic weapon
b. Is belt or magazine fed
c. Fires from the close bolt position
d. Is recoil operated
The M249 tripping lever is attached to the?
a. Sear b. Bolt c. Safety d. None of the above

## Slide 12
M249 WRITTEN PE
What is the corrective action for a plugged gas regulator (mono-block) on the M249?
a. (O) b. (H) c. (F) d. (D)
On the M249, a failure to extract could be caused by?
a. Ejector worn b. Insufficient gas pressure c. Loose tower d. Firing pin damaged
8. A defective M249 sear could cause a failure to?
a. Lock b. Feed c. Cock d. Unlock
The M249 machine gun
a. Is a semi-automatic weapon
b. Is belt or magazine fed
c. Fires from the close bolt position
d. Is recoil operated
The M249 tripping lever is attached to the?
a. Sear b. Bolt c. Safety d. None of the above

## Slide 13
M249 WRITTEN PE
11. On the M249, a failure to charge could be caused by?
a. Frame trigger c. Bent arm on the cocking handle
b. Shoulder rest d. None of these
12. The first check in a failure to chamber the M249 is?
a. Check for defective buffer c. Check for spent cartridge
b. Charging handle d. None of these
13. A failure to fire the M249 could be caused by?
a. Firing pin tip damaged c. Burred rear cartridge retaining pins
b. Feed pawl assembly is sticking d. All of these
On the M249, the first step in troubleshooting a failure to fire is?
a. Check for improperly installed firing pin b. Check for loose gas collar
c. Check for broken firing pin d. None of the above
A damaged M249 sear will result in a failure to?
a. Eject. b. Lock c. Cock. d. Chamber.

## Slide 14
M249 WRITTEN PE
11. On the M249, a failure to charge could be caused by?
a. Frame trigger c. Bent arm on the cocking handle
b. Shoulder rest d. None of these
12. The first check in a failure to chamber the M249 is?
a. Check for defective buffer c. Check for spent cartridge
b. Charging handle d. None of these
13. A failure to fire the M249 could be caused by?
a. Firing pin tip damaged c. Burred rear cartridge retaining pins
b. Feed pawl assembly is sticking d. All of these
On the M249, the first step in troubleshooting a failure to fire is?
a. Check for improperly installed firing pin b. Check for loose gas collar
c. Check for broken firing pin d. None of the above
A damaged M249 sear will result in a failure to?
a. Eject. b. Lock c. Cock. d. Chamber.

## Slide 15
M249 WRITTEN PE
11. On the M249, a failure to charge could be caused by?
a. Frame trigger c. Bent arm on the cocking handle
b. Shoulder rest d. None of these
12. The first check in a failure to chamber the M249 is?
a. Check for defective buffer c. Check for spent cartridge
b. Charging handle d. None of these
13. A failure to fire the M249 could be caused by?
a. Firing pin tip damaged c. Burred rear cartridge retaining pins
b. Feed pawl assembly is sticking d. All of these
On the M249, the first step in troubleshooting a failure to fire is?
a. Check for improperly installed firing pin b. Check for loose gas collar
c. Check for broken firing pin d. None of the above
A damaged M249 sear will result in a failure to?
a. Eject. b. Lock c. Cock. d. Chamber.

## Slide 16
M249 WRITTEN PE
11. On the M249, a failure to charge could be caused by?
a. Frame trigger c. Bent arm on the cocking handle
b. Shoulder rest d. None of these
12. The first check in a failure to chamber the M249 is?
a. Check for defective buffer c. Check for spent cartridge
b. Charging handle d. None of these
13. A failure to fire the M249 could be caused by?
a. Firing pin tip damaged c. Burred rear cartridge retaining pins
b. Feed pawl assembly is sticking d. All of these
On the M249, the first step in troubleshooting a failure to fire is?
a. Check for improperly installed firing pin b. Check for loose gas collar
c. Check for broken firing pin d. None of the above
A damaged M249 sear will result in a failure to?
a. Eject. b. Lock c. Cock. d. Chamber.

## Slide 17
M249 WRITTEN PE
11. On the M249, a failure to charge could be caused by?
a. Frame trigger c. Bent arm on the cocking handle
b. Shoulder rest d. None of these
12. The first check in a failure to chamber the M249 is?
a. Check for defective buffer c. Check for spent cartridge
b. Charging handle d. None of these
13. A failure to fire the M249 could be caused by?
a. Firing pin tip damaged c. Burred rear cartridge retaining pins
b. Feed pawl assembly is sticking d. All of these
On the M249, the first step in troubleshooting a failure to fire is?
a. Check for improperly installed firing pin b. Check for loose gas collar
c. Check for broken firing pin d. None of the above
A damaged M249 sear will result in a failure to?
a. Eject. b. Lock c. Cock. d. Chamber.

## Slide 18
M249 WRITTEN PE
11. On the M249, a failure to charge could be caused by?
a. Frame trigger c. Bent arm on the cocking handle
b. Shoulder rest d. None of these
12. The first check in a failure to chamber the M249 is?
a. Check for defective buffer c. Check for spent cartridge
b. Charging handle d. None of these
13. A failure to fire the M249 could be caused by?
a. Firing pin tip damaged c. Burred rear cartridge retaining pins
b. Feed pawl assembly is sticking d. All of these
On the M249, the first step in troubleshooting a failure to fire is?
a. Check for improperly installed firing pin b. Check for loose gas collar
c. Check for broken firing pin d. None of the above
A damaged M249 sear will result in a failure to?
a. Eject. b. Lock c. Cock. d. Chamber.

## Slide 19
M249 WRITTEN PE
The M249 extraction begins while the unlocking cycle in going on?
a. True
b. False
Which part of the M249 gas system should never be lubricated?
a. Piston b. Regulator c. Gas tube d. All of the above
What component on the M249 houses the firing pin and roller assembly?
a, Bolt and piston assembly b. Slide assembly
c. Feed tray assembly d. Buttstock assembly
PMCS for the M249 machine gun are scheduled how often?
a. Daily b. Weekly c. Quarterly d. Monthly
A broken driving spring could cause a failure to feed on the M249, what other cycle of function could it cause a failure in?
a. Cock b. Fire c. Unlock d. Chamber

## Slide 20
M249 WRITTEN PE
The M249 extraction begins while the unlocking cycle in going on?
a. True
b. False
Which part of the M249 gas system should never be lubricated?
a. Piston b. Regulator c. Gas tube d. All of the above
What component on the M249 houses the firing pin and roller assembly?
a, Bolt and piston assembly b. Slide assembly
c. Feed tray assembly d. Buttstock assembly
PMCS for the M249 machine gun are scheduled how often?
a. Daily b. Weekly c. Quarterly d. Monthly
A broken driving spring could cause a failure to feed on the M249, what other cycle of function could it cause a failure in?
a. Cock b. Fire c. Unlock d. Chamber

## Slide 21
M249 WRITTEN PE
The M249 extraction begins while the unlocking cycle in going on?
a. True
b. False
Which part of the M249 gas system should never be lubricated?
a. Piston b. Regulator c. Gas tube d. All of the above
What component on the M249 houses the firing pin and roller assembly?
a, Bolt and piston assembly b. Slide assembly
c. Feed tray assembly d. Buttstock assembly
PMCS for the M249 machine gun are scheduled how often?
a. Daily b. Weekly c. Quarterly d. Monthly
A broken driving spring could cause a failure to feed on the M249, what other cycle of function could it cause a failure in?
a. Cock b. Fire c. Unlock d. Chamber

## Slide 22
M249 WRITTEN PE
The M249 extraction begins while the unlocking cycle in going on?
a. True
b. False
Which part of the M249 gas system should never be lubricated?
a. Piston b. Regulator c. Gas tube d. All of the above
What component on the M249 houses the firing pin and roller assembly?
a, Bolt and piston assembly b. Slide assembly
c. Feed tray assembly d. Buttstock assembly
PMCS for the M249 machine gun are scheduled how often?
a. Daily b. Weekly c. Quarterly d. Monthly
A broken driving spring could cause a failure to feed on the M249, what other cycle of function could it cause a failure in?
a. Cock b. Fire c. Unlock d. Chamber

## Slide 23
M249 WRITTEN PE
The M249 extraction begins while the unlocking cycle in going on?
a. True
b. False
Which part of the M249 gas system should never be lubricated?
a. Piston b. Regulator c. Gas tube d. All of the above
What component on the M249 houses the firing pin and roller assembly?
a, Bolt and piston assembly b. Slide assembly
c. Feed tray assembly d. Buttstock assembly
PMCS for the M249 machine gun are scheduled how often?
a. Daily b. Weekly c. Quarterly d. Monthly
A broken driving spring could cause a failure to feed on the M249, what other cycle of function could it cause a failure in?
a. Cock b. Fire c. Unlock d. Chamber

## Slide 24
M249 WRITTEN PE
The M249 extraction begins while the unlocking cycle in going on?
a. True
b. False
Which part of the M249 gas system should never be lubricated?
a. Piston b. Regulator c. Gas tube d. All of the above
What component on the M249 houses the firing pin and roller assembly?
a, Bolt and piston assembly b. Slide assembly
c. Feed tray assembly d. Buttstock assembly
PMCS for the M249 machine gun are scheduled how often?
a. Daily b. Weekly c. Quarterly d. Monthly
A broken driving spring could cause a failure to feed on the M249, what other cycle of function could it cause a failure in?
a. Cock b. Fire c. Unlock d. Chamber

## Slide 25
M249 WRITTEN PE
21. What is the status symbol for a M249 chipped ejector tip when the fault is listed on the DA Form 5988-E?
a. O b. X c. / d. F
22. What is the difference between the old and new style M249 barrels?
a. Gas Regulator/Mono Block b. Handle c. Sights d. Spring
23. All M249 barrels should be gauged and have a 100% technical inspection how often?
a. Semi-annually b. Annually c. Quarterly d. Monthly
24. What does the SMR code of XA mean?
a. Do not requisition, order the next higher assembly b. Order it using the CAGEC and part number
c. Identified by manufacturer's part number d. Item is not stocked, local purchase
25. What three parts of the M249 trigger mechanism, if defective, could cause a failure to cock?
a. Sear, sear spring, trigger b. Trigger, sear, safety
c. Sear, sear spring, tripping lever d. Sear, safety, tripping lever

## Slide 26
M249 WRITTEN PE
21. What is the status symbol for a M249 chipped ejector tip when the fault is listed on the DA Form 5988-E?
a. O b. X c. / d. F
22. What is the difference between the old and new style M249 barrels?
a. Gas Regulator/Mono Block b. Handle c. Sights d. Spring
23. All M249 barrels should be gauged and have a 100% technical inspection how often?
a. Semi-annually b. Annually c. Quarterly d. Monthly
24. What does the SMR code of XA mean?
a. Do not requisition, order the next higher assembly b. Order it using the CAGEC and part number
c. Identified by manufacturer's part number d. Item is not stocked, local purchase
25. What three parts of the M249 trigger mechanism, if defective, could cause a failure to cock?
a. Sear, sear spring, trigger b. Trigger, sear, safety
c. Sear, sear spring, tripping lever d. Sear, safety, tripping lever

## Slide 27
M249 WRITTEN PE
21. What is the status symbol for a M249 chipped ejector tip when the fault is listed on the DA Form 5988-E?
a. O b. X c. / d. F
22. What is the difference between the old and new style M249 barrels?
a. Gas Regulator/Mono Block b. Handle c. Sights d. Spring
23. All M249 barrels should be gauged and have a 100% technical inspection how often?
a. Semi-annually b. Annually c. Quarterly d. Monthly
24. What does the SMR code of XA mean?
a. Do not requisition, order the next higher assembly b. Order it using the CAGEC and part number
c. Identified by manufacturer's part number d. Item is not stocked, local purchase
25. What three parts of the M249 trigger mechanism, if defective, could cause a failure to cock?
a. Sear, sear spring, trigger b. Trigger, sear, safety
c. Sear, sear spring, tripping lever d. Sear, safety, tripping lever

## Slide 28
M249 WRITTEN PE
21. What is the status symbol for a M249 chipped ejector tip when the fault is listed on the DA Form 5988-E?
a. O b. X c. / d. F
22. What is the difference between the old and new style M249 barrels?
a. Gas Regulator/Mono Block b. Handle c. Sights d. Spring
23. All M249 barrels should be gauged and have a 100% technical inspection how often?
a. Semi-annually b. Annually c. Quarterly d. Monthly
24. What does the SMR code of XA mean?
a. Do not requisition, order the next higher assembly b. Order it using the CAGEC and part number
c. Identified by manufacturer's part number d. Item is not stocked, local purchase
25. What three parts of the M249 trigger mechanism, if defective, could cause a failure to cock?
a. Sear, sear spring, trigger b. Trigger, sear, safety
c. Sear, sear spring, tripping lever d. Sear, safety, tripping lever

## Slide 29
M249 WRITTEN PE
21. What is the status symbol for a M249 chipped ejector tip when the fault is listed on the DA Form 5988-E?
a. O b. X c. / d. F
22. What is the difference between the old and new style M249 barrels?
a. Gas Regulator/Mono Block b. Handle c. Sights d. Spring
23. All M249 barrels should be gauged and have a 100% technical inspection how often?
a. Semi-annually b. Annually c. Quarterly d. Monthly
24. What does the SMR code of XA mean?
a. Do not requisition, order the next higher assembly b. Order it using the CAGEC and part number
c. Identified by manufacturer's part number d. Item is not stocked, local purchase
25. What three parts of the M249 trigger mechanism, if defective, could cause a failure to cock?
a. Sear, sear spring, trigger b. Trigger, sear, safety
c. Sear, sear spring, tripping lever d. Sear, safety, tripping lever

## Slide 30
M249 WRITTEN PE
21. What is the status symbol for a M249 chipped ejector tip when the fault is listed on the DA Form 5988-E?
a. O b. X c. / d. F
22. What is the difference between the old and new style M249 barrels?
a. Gas Regulator/Mono Block b. Handle c. Sights d. Spring
23. All M249 barrels should be gauged and have a 100% technical inspection how often?
a. Semi-annually b. Annually c. Quarterly d. Monthly
24. What does the SMR code of XA mean?
a. Do not requisition, order the next higher assembly b. Order it using the CAGEC and part number
c. Identified by manufacturer's part number d. Item is not stocked, local purchase
25. What three parts of the M249 trigger mechanism, if defective, could cause a failure to cock?
a. Sear, sear spring, trigger b. Trigger, sear, safety
c. Sear, sear spring, tripping lever d. Sear, safety, tripping lever

## Slide 31
M249 WRITTEN PE
26. The M249 cycle of functioning begins and ends when?
a. Sear, sear spring, tripping lever b. At the open bolt position
c. Cocking d. Feeding
27. The M249 features fixed headspace which permits what?
a. Cocking and locking b. Chambering and firing c. Rapid barrel changes d. Feeding and extracting
28. What is the sustained rate of fire for the M249?
a.1000 rpm b. 850 rpm c. 725 rpm d. 100 rpm
29. What two roles can the M249 operate in?
a. AR and LMG roles b. AK and GML roles c. OK and OMG roles d. GP and AGR roles

## Slide 32
M249 WRITTEN PE
26. The M249 cycle of functioning begins and ends when?
a. Sear, sear spring, tripping lever b. At the open bolt position
c. Cocking d. Feeding
27. The M249 features fixed headspace which permits what?
a. Cocking and locking b. Chambering and firing c. Rapid barrel changes d. Feeding and extracting
28. What is the sustained rate of fire for the M249?
a.1000 rpm b. 850 rpm c. 725 rpm d. 100 rpm
29. What two roles can the M249 operate in?
a. AR and LMG roles b. AK and GML roles c. OK and OMG roles d. GP and AGR roles

## Slide 33
M249 WRITTEN PE
26. The M249 cycle of functioning begins and ends when?
a. Sear, sear spring, tripping lever b. At the open bolt position
c. Cocking d. Feeding
27. The M249 features fixed headspace which permits what?
a. Cocking and locking b. Chambering and firing c. Rapid barrel changes d. Feeding and extracting
28. What is the sustained rate of fire for the M249?
a.1000 rpm b. 850 rpm c. 725 rpm d. 100 rpm
29. What two roles can the M249 operate in?
a. AR and LMG roles b. AK and GML roles c. OK and OMG roles d. GP and AGR roles

## Slide 34
M249 WRITTEN PE
26. The M249 cycle of functioning begins and ends when?
a. Sear, sear spring, tripping lever b. At the open bolt position
c. Cocking d. Feeding
27. The M249 features fixed headspace which permits what?
a. Cocking and locking b. Chambering and firing c. Rapid barrel changes d. Feeding and extracting
28. What is the sustained rate of fire for the M249?
a.1000 rpm b. 850 rpm c. 725 rpm d. 100 rpm
29. What two roles can the M249 operate in?
a. AR and LMG roles b. AK and GML roles c. OK and OMG roles d. GP and AGR roles

## Slide 35
M249 WRITTEN PE
26. The M249 cycle of functioning begins and ends when?
a. Sear, sear spring, tripping lever b. At the open bolt position
c. Cocking d. Feeding
27. The M249 features fixed headspace which permits what?
a. Cocking and locking b. Chambering and firing c. Rapid barrel changes d. Feeding and extracting
28. What is the sustained rate of fire for the M249?
a.1000 rpm b. 850 rpm c. 725 rpm d. 100 rpm
29. What two roles can the M249 operate in?
a. AR and LMG roles b. AK and GML roles c. OK and OMG roles d. GP and AGR roles

## Slide 36
M249 WRITTEN PE
30. The EQUIPMENT NOT READY/AVAILABLE IF column indicates what?
a. Item to be checked or serviced
b. When to do the check or service
c. Deficiencies that must be corrected before MG can be operated
d. The M249 is returned to its containment area.

## Slide 37
M249 WRITTEN PE
30. The EQUIPMENT NOT READY/AVAILABLE IF column indicates what?
a. Item to be checked or serviced
b. When to do the check or service
c. Deficiencies that must be corrected before MG can be operated
d. The M249 is returned to its containment area.