## Slide 1: LUBRICATION

## Slide 2: Rifle Bore Cleaner (RBC)
NSN 6850-00-224-6577
Cleaner only, not a lubricant
Must be followed by some lubricant
2oz bottle, 8oz &1gal can available

## Slide 3: Lubricating Oil, Arctic, Weapons (LAW)
NSN 9150-00-292-9689
Temperature must be below 100 F
1qt can available

## Slide 4: Grease, Molybdenum Disulfide (GMD)
NSN 9150-00-935-4018
Recommended for MK19
14oz tube, 6.5lb & 35lb can available

## Slide 5: Cleaner, Lubricant, Preservative (CLP)
NSN 9150-01-079-6124
Do not use on MK19
Only lube used on M249
Do not mix with any other lubricant
½oz & 4oz bottles, 1pt, 1gal available

## Slide 6: Lubricant, Semi-Fluid, Automatic Weapon (LSA)
NSN 9150-00-889-3522
Never mix with CLP
Clean weapon with cleaning compound solvent MIL-PRF-680 if CLP was used
Use on MK19 if GMD in unavailable
2oz, 4oz & 32oz bottles, 1gal can available

## Slide 7: Lubricant, Semi-Fluid, Automatic Weapon W/Teflon (LSA-T)
NSN 9150-00-949-0323
Do not mix with CLP
Clean weapon with cleaning compound solvent MIL-PRF-680 if CLP was used
Use on MK19 if GMD is unavailable
8oz tube, 1lb can available

## Slide 8: Solid Film Lubricant (SFL)
NSN 9150-01-260-2534
Touch up to 1/3 weapon exterior
Weapon must be cleaned with cleaning compound solvent MIL-PRF-680 first before use
16oz aerosol can, 1qt & 1gal can available

## Slide 9
Reference: PS Magazine Issue 787, Dated June 2018

## Slide 10: MIL-PRF-680 Type II Dry Cleaning Compound Solvent
No Photo Available
Replaces P-D-680 dry cleaning solvent as of July 2005
Recommended for use in solvent tanks
Must be followed by lubricant
1gal 6850-01-474-2319
5gal 6850-01-474-2317
15gal 6850-01-378-0698
55gal 6850-01-474-2316

## Slide 11: DON’T:
Use oven and carburetor cleaner: Strips off protective finish, leads to corrosion
Use cleaning pads (Green scratch pads): Strips off protective finish, leads to corrosion
Use shaving cream or Simple Green: Removes all lubrication, leads to corrosion
Use lightweight oils (WD40, etc): Evaporates quickly, low flash point

## Slide 12: DON’T
Use cotton tips or swabs: Cotton plugs small areas such as gas ports. Use swabs only in weapon barrels.
Use chamber brush attached to a drill: Grinds off metal
Use homemade cleaning tools (coat hangers): Scratches metal/protective finish
Use paper towels and rags: Clogs areas like buffer tubes

## Slide 13: DON’T
Use JP-8: Causes worse carbon build-up, difficult to remove
Use motor oil: Hardens, heavy carbon build-up
Use graphite-based lubricants: Eats and destroys aluminum and other alloys
Use sandpaper: Scratches metal/Protective finish

## Slide 14: For NSN’s and more information on lubrication
Expendable and Durable Items List in the TM -23&P
https://www.logsa.army.mil/psmag/archives/PS2008/671/671-23.pdf
TACOM Ground Precautionary Message 07-003